## Slide 1
Surfactant-Enhanced Spontaneous Imbibition in Oil-Wet, Heavy Oil Bearing Carbonate Formations
Amir Amini
Maura Puerto
Clarence Miller
George Hirasaki
April 23, 2012

## Slide 2: Formation
Dead Oil: API ~ 21
Viscosity: ~150 cp (dead oil @ 40oC)
Temperature: 40oC
Formation Brine (FB): TDS ~ 7800 mg/L
(significant amount of divalent ions)
River Water (RW): TDS ~ 280 mg/L

## Slide 3
Salinity Scan: Mixtures of FB and RW
% FB 0 10 20 30 40 50 60 70 80 90 100
near optimal salinity
Surfactant Phase Behavior at 40oC
BLEND: 1% S13D = iC13-13PO Sulfate + 0.1% S2= IOS 15-18
Both surfactants from Stepan
40oC
Aqueous Solution
30% FB / 70% RW
Graduated pipette on back of sample for demonstrating clarity
Clear solution suitable for studies
of adsorption and core testing
emulsions

## Slide 4
Static Adsorption of 1% S13D + 0.1% S2 in 30% FB / 70% RW
Aqueous Phase
Organic Phase
s
BET surface area = 1.8 m2/g
about an order of magnitude lower adsorption is expected in the reservoir rock

## Slide 5: Overall Procedure for Spontaneous Imbibition
Insert core in core-holder to determine properties : k, ø, kro , etc.
Saturate core with formation brine (FB), k and ø.
Displace FB with dead oil to connate water, kro end-point.
Prepare coreholder (i.e., insert back pressure regulator, venting to the hood) and age at elevated temperatures for making core oil-wet.
Insert aged core in an Amott cell, first filled with the brine and next with the surfactant solution. Measure oil production in Amott cell at 40oC as a function of time.

## Slide 6: Coreflood Setup for 1.5” Silurian Dolomite and Reservoir Cores
Actual Experimental Set-Up
Transducer
Isco Pump
CoreHolder
Core Holder
Transducer
Computer
ISCO
Pump
Graduated Collector
Filter

## Slide 7: Summary of Core Preparation Results
Core | Formation | Dimensions D × L | Porosity (Ø) | Brine Permeability (k) | Irreducible Water Saturation (Swi) | Endpoint Oil Relative Permeability (kro)
Silurian Dolomite | Thornton | 1.5”× 3.7” | 20.9 % | 400 mD | 16.3 % | 0.6
Reservoir |  | 1.5”× 3.3” | 20.7% | 15 mD | 35 % | 0.3
Oil saturated Silurian core after being Oil saturated Silurian core after being
aged for 10 days at 100oC (side view) aged for 10 days at 100oC (top view)

## Slide 8: Spontaneous Imbibition Experiment
Silurian core inside the After being in contact with
imbibition cell (empty cell) formation brine for 4 days
No oil was produced
brine
meniscus

## Slide 9
After ~ 1 min of being in
contact with the surfactant solution at room temperature
Considerable amount of oil that was
produced was not collected at top of
the Amott cell; instead it formed
oil in water emulsion or microemulsion
and remained in the body of the cell
40oC
Practically no oil was produced
from the reservoir cores

## Slide 10
NB-1 : Inverse Bond Number
capillary force versus gravity
N­B-1 << 1 is needed for spontaneous imbibition to be gravity driven. For the reservoir cores where N­B-1 ­­­­­­~ 1 with initial water saturation, gravity forces are too weak to generate an upward flow of oil.

## Slide 11: Wettability on Calcite Plates
Initial coverage
After 2 hours
After 18 hours
Upward streaming of oil
Immersed in surfactant
formulation (T = 40oC)
(T = 40oC)
Oil drop on an 18mm×18mm oil-wet marble plate, immersed in the formation brine.
Oil drop on the same marble plate, immersed in the surfactant formulation for 18 hours.
1mm
(T = 40oC)
ϴA ~ 170o
ϴA ~ 140o

## Slide 12: IFT Between the Surfactant Solution and the Oil
A drop of oil suspended inside the spinning
capillary tube filled with the surfactant solution
drop of oil
+ (equilibrated)
surfactant formulation
T = 40oC
drop of oil
+ (not equilibrated)
surfactant formulation
T = 40oC
IFT = 8.0 × 10 - 3 mN/m
IFT = 1.3 × 10 - 2 mN/m

## Slide 13: Summary
About 30% of the OOIP in the Silurian core was recovered.
Barely any oil was produced from the reservoir cores.
The formulation was not able to alter the wettability of initially oil-wet calcite plates to water-wet.
The measured IFT of the surfactant formulation against the deal crude oil (10-2mN/m) was not sufficiently low to produce the high viscosity oil from the low permeability cores.

## Slide 14
Thank
You!