## Slide 1: Live oil – surfactant phase behavior
Aparna Sagi, Maura Puerto, Clarence Miller, George Hirasaki
April 23, 2012

## Slide 2: Introduction
Surfactants  ultra low IFT  EOR
Optimal salinity (ultra-low IFT) for a surfactant system dependent on
  Oil composition: dead vs live oil
  Temperature, pressure, WOR, etc
Objective:
  Determine and compare surfactant optimal salinity for dead and live crude oil (CO2, CH4,C2H6)

## Slide 3: System description
Temperature: 30ºC
Surfactant: S13D/S2 (90/10 wt.) 1wt% (aq.)
  S13D: iC13 -13PO sulfate
  S2: C15-18 internal olefin sulfonate
Brine: 11,000ppm (incl. Ca2+, Mg2+) – TB2
Crude oil: 28º API (dead) with
  No dissolved gas (dead oil)
  Methane @ 600psi
  Ethane @ 50psi, 95psi
  Carbon dioxide @ 60psi, 600psi

## Slide 4: Experimental procedure – dead oil
Optimal salinity
Winsor Type - I
Winsor Type - II
Varying salinity
Winsor Type - III
micro
micro
Pipette (bottom sealed)
Brine + surfactant
Oil
Initial interface
Seal open end
24 hr

## Slide 5: Experimental procedure – live oil
P
Gas
Make live oil
P
Gas
Oil
Purge cell of air
Inject surf. solution
P
Surf. soln.
Inc. temp. to 30°C
P
Hand mix sample
Observe phases
P

## Slide 6: Results – dead oil
70% 80% 90% 100% 110% 120%
Salinity (% TB2)
Type I
Type I
Type II
Type II
Type II
Type I
OIL
MICRO EMULSION
WATER
MACRO EMULSION
Vo/Vs ~ 6
Optimal
Initial w/o interface

## Slide 7: Results – Methane @ 600psi
50% 70% 90% 110%
Salinity (% TB2)
Type I
Type I
Type II
Type II
OIL
MICRO EMULSION
WATER
MACRO EMULSION
Optimal
Initial w/o interface

## Slide 8: Results – Ethane @ 50psi
50% 60% 70% 80%
Salinity (% TB2)
Type I
Type I
Type I
Type II
OIL/ OIL+MACRO
MICRO EMULSION
WATER
MACRO
Vo/Vs ~ 13
Optimal
Initial w/o interface

## Slide 9: Results – Ethane @ 95psi
30% 40% 50% 60%
Salinity (% TB2)
Type I
Type I
??
Type II
OIL
MICRO EMULSION
WATER
MACRO
Optimal
Initial w/o interface

## Slide 10: Results – CO2 @ 60psi
70% 80% 90% 100%
Salinity (% TB2)
Type I
Type I
Type I
Type II
OIL
MICRO EMULSION
WATER
MACRO
Optimal
Initial w/o interface

## Slide 11: Results –CO2 @ 600psi
10% 20% 30% 40% 50%
Salinity (% TB2)
Type I
Type I
Type I
Type II
Type II
OIL
MICRO EMULSION
WATER
MACRO
Optimal
Initial w/o interface

## Slide 12: Consolidated results
Methane
CO2
Ethane

## Slide 13: Conclusions
The effect of dissolved gas (upto 600psi) on surfactant optimal salinity (CØ) has been demonstrated
  Methane
    Slight decrease in optimal salinity
  Carbon dioxide
    Decrease in the optimal salinity
  Ethane
    Substantial decrease in optimal salinity

## Slide 14: QUESTIONS

## Slide 15
P