## Slide 1: Surfactant System Selection to Generate foam for EOR Application
AmirHosein Valiollahzadeh
Maura Puerto
Jose Lopez
Astron Liu
Lisa Biswal
George Hirasaki

## Slide 2
suitable to reservoir conditions:
temperature, salinity, tolerable to divalent ions (
Low retention to:
  Oil phase
  Rock (adsorption)
Strong foam in presence of oil
- blending with foam booster Zwitterionic surfactant: Betaine
Lowering Interfacial Tension between oil and water
Desired Surfactant system

## Slide 3
1- Alpha Olefin Sulfonate (AOS C14-16)
-widely used but not tolerable with divalent ions
2- Lauryl and Myristyl Betaine (LB)
-known as a foam booster
3- Orthoxylene Sulfonate- C24 (OXS)
-more hydrophobic will decrease IFT
4- Anionic surfactant (A)
-proprietary surfactant that may also help reduce IFT
List of surfactants in this study

## Slide 4
ions | Injection Water | Formation Brine | Sea Water*
HCO3- | 402 | 834 | 140
Cl- | 20,140 | 86,291 | 18,980
S042- | 201 | 595 | 2,649
Ca2+ | 1,536 | 12,224 | 400
Mg2+ | 826 | 2,189 | 1,262
Na+,K+ | 9,970 | 38,336 | 10,556
Total Salinity mg/l | 33,070 | 140,470 | 34,483
Ion composition in mg/l
*Geochemistry of oilfield waters By A. Gene Collin
Injection Water and Formation Brine

## Slide 5
Phase behavior Experiments:
Blend Scan (vary ratio of surfactants) to obtain the optimal blend
  - aqueous
  - n-octane
  - Crude oil
Salinity Scan (vary ion concentration) to determine the optimal salinity
Surfactant Phase Behavior

## Slide 6: Crude Oil – odor and treatment
Chart: Time (min)
| 0 | 8.3335833333333351 | 16.666666666666671 | 25 | 33.333333333333343 | 41.666666666666643 | 50.000166666666637 | 58.333333333333343 | 66.666666666666671 | 75
crude oil + Toluene + Molecular Sieves | 45.413 | 32.534 | 27.779 | 25.405 | 23.869 | 23.007 | 22.332 | 21.79 | 21.258 | 21.061
Crude oil | 8.287 | 7.912 | 8.076 | 7.848 | 7.856 | 8.007 | 7.867 | 7.812 | 7.706 | 7.411
crude oil + Toluene | 5.637 | 5.129 | 4.9 | 4.679 | 4.664 | 4.63 | 4.593 | 4.663 | 4.652 | 4.655
Molecular Sieve used:
SIGMA-ALDRICH 4Å type
composition:
1 Na2O: 1 Al2O3: 2.0 ± 0.1 SiO2: x H2O.
Effective pore opening :
4Å
Adsorbed species:
SO2, CO2, H2S, C2H4, C2H6, and C3H6
Removing Mercaptan as well as other possible contaminants
Crude Oil Issues – odor and treatment

## Slide 7: LB:AOS Blend Scan in Injection Water with n-Octane and crude oil. 2% overall surfactant concentration. WOR~1. 60°C
LB 9/1 8/2 7/3 6/4 5/5 4/6 3/7 2/8 1/9 AOS
Winsor Type I:
Lower phase micro-emulsion
n-Octane
Crude oil

## Slide 8
LB 9/1 8/2 7/3 6/4 5/5 4/ 6 3/7 2/8 1/9 AOS
25°C
60°C
Injection composition
Aqueous blend scan LB:AOS in Injection water. 1% surfactant concentration

## Slide 9
25°C
60°C
Inj 9/1 8/2 7/3 6/4 5/5 4/6 3/7 2/8 1/9 FB
7:3 LB:AOS Aqueous Salinity Scan from Injection Water to Formation Brine. 1% Overall Surfactant Concentration

## Slide 10
Inj 9/1 8/2 7/3 6/4 5/5 4/6 3/7 2/8 1/9 FB
7:3 LB:AOS Salinity Scan from Injection Water to Formation Brine
2% Overall Surfactant Concentration. 60°C
Winsor Type I:
Lower phase micro-emulsion

## Slide 11
LB:OXS Blend Scan in Injection Water with n-Octane. 2% overall surfactant concentration
LB:OXS aqueous Blend Scan in Injection Water 1% surfactant concentration. 60°C
Winsor Type I:
Lower phase micro-emulsion
n-octane
aqueous

## Slide 12
LB:A Blend Scan in Injection Water with n-Octane and crude oil. 2% overall surfactant concentration. WOR~1. 60°C
LB 9/1 8/2 7/3 6/4 5/5 4/6 3/7 2/8 1/9 A
LB 9/1 8/2 7/3 6/4 5/5 4/6 3/7 2/8 1/9 A
Winsor Type I:
Lower phase micro-emulsion
Winsor Type II:
Upper phase micro-emulsion

## Slide 13
LB:A Surfactant Aqueous Blend Scan in Injection Water. 1% Overall Surfactant Concentration
LB 9/1 8/2 7/3 6/4 5/5 4/6 3/7 2/8 1/9 A
Injection composition
25°C
60°C

## Slide 14
Winsor Type I:
Lower phase micro-emulsion
n-octane
aqueous
9:1 LB:A Salinity Scan from Injection Water to Formation Brine
2% Overall Surfactant Concentration. 60°C
Inj 9/1 8/2 7/3 6/4 5/5 4/6 3/7 2/8 1/9 FB

## Slide 15
Transport of components and phases in a surfactant/foam EOR process for a giant carbonate Reservoir, PhD thesis 2012 by Jose Lopez.
Dynamic Test: Homogenous 1-D Sand Pack

## Slide 16
Chart: PV Liquid injected
 | 120 | 0
Injection condition: 0.2 ml/min surf + 0.8 Sccm3/min
Quality at steady state at test condition: 0.45 and 0.55 corresponding to 1st and 2nd internal tap
Apparent Viscosity at steady state: 800 and 630 cP corresponding to 1st and 2nd internal tap
Test results of AOS C14-16 in injection water
Notes: Test results of AOS C14-16 in injection water
Injection condition: 0.2 ml/min surf + 0.8 Sccm3/min
Quality at St.St at test condition: 0.45 and 0.55 corresponding to 1st and 2nd internal tap
Apparent Viscosity at St.St: 800 and 875 cP

## Slide 17
Chart: PV Liquid injected
 | 120 | 0
Injection condition: 1 ml/min surf + 10 Sccm3/min
Quality at steady state: 0.6 and 0.7 corresponding to 1st and 2nd internal tap
Apparent Vis at steady state: 200, 145 cP corresponding to 1st and 2nd internal tap
Test results of LB:AOSC14-16 7:3 in injection water

## Slide 18
Chart: LB-X (SW, 94C) G =0.6-0.8
| 27.140641975956299 | 13.651381389772499 | 5.5703495240294609 | 3.4767444356368951 | 43.241285831598653
 | 0.45448 | 0.82325 | 1.6731 | 2.4914 | 0.32963
 | 6.7571 | 4.8693 | 3.5088 | 2.5285 | 1.8221 | 1.313 | 0.94617 | 0.68182 | 0.49132 | 0.35405 | 0.25513 | 0.18385
Carreau, 1997
Rheology of polymeric systems
Addapted from Lopez, Thesis 2012
Shear Thinning effect; Comparison with other studies

## Slide 19
Chart: LB-X (SW, 94C) G =0.6-0.8
| 27.140641975956299 | 13.651381389772499 | 5.5703495240294609 | 3.4767444356368968 | 43.24128583159866
 | 0.45448 | 0.82325 | 1.6731 | 2.4914 | 0.32963
 | 6.7571 | 4.8693 | 3.5088 | 2.5285 | 1.8221 | 1.313 | 0.94617 | 0.68182 | 0.49132 | 0.35405 | 0.25513 | 0.18385
 | 0.8 | 0.63
 | 0.2 | 0.145
Carreau, 1997
Rheology of polymeric systems
Addapted from Lopez, Thesis 2012
Shear Thinning effect; Comparison with other studies

## Slide 20
Conclusion and Future plans
LB:AOSC14-16 7:3 is a clear solution at reservoir temperature and salinity
LB:A has an optimal blend ratio at injection salinity. This system could have a lower IFT between oil and brine than LB:AOSC14-16 system.
LB:AOSC14-16 7:3 generates strong foam in reservoir temperature in absence of oil.
Future Plan
Investigate whether LB:A system has lower IFT between oil and brine than LB:AOSC14-16 system and also capable of generating strong foam
More foam tests with AOS C14-16 and LB:AOSC14-16 to find effect of quality, surfactant concentration and flow rate
Foam tests in presence of oil

## Slide 21
Acknowledgement to our Sponsor: