## Slide 1
Qualitative and quantitative study of foam
for Transport of Phases
in a Surfactant/Foam EOR Process for a Giant Carbonate Reservoir
José Luis López-Salinas
Maura C. Puerto
George J. Hirasaki
Clarence A. Miller
Rice University
April 2013

## Slide 2: Outline
Introduction
Foaming surfactants in seawater at 94°C.
Foam behavior in presence of oil.
Mathematical model for foam
Challenges of foam models for applications in fractured reservoirs
Mimic of oil recovery from matrix using foam in fractures (qualitative study in micro-channels)
Conclusions

## Slide 3
Introduction
The transport of components and phases plays a fundamental role in the success of an EOR process. Because many reservoirs have harsh conditions of salinity, temperature and rock heterogeneity, which limit process options, a robust system with flexibility is required.

## Slide 4
Conditions for mobility control and
improved displacement efficiency with foam
In a fractured reservoir, the success of surfactant flooding depends on how effectively the surfactant residing in the fracture can penetrate and propagate into the matrix. Thus it is believed that gravity-induced spontaneous imbibition best represents what will happen in fractured reservoirs. Introduction of alkaline / surfactant solution overcomes capillary forces by both wettablity alteration and IFT reduction.
Foam flowing in permeable media can drastically reduce the mobility of a gas phase. The mobility is less than the single-phase mobility of water and is substantially less than the single-phase mobility of the gas phase. Foams are potentially suitable for improving displacement efficiency in a process or for blocking or restricting the flow of injected fluids in high permeability streaks
Danhua Zhang. Surfactant-Enhanced Oil Recovery Process For A Fracturated, Oil-wet Carbonate Reservoir.
Rice University Thesis CH.E 2006 ZHANG
L.W. Lake. Enhanced Oil Recovery. Prentice Hall, 1989
D.W. Green and G.P. Willhite. Enhanced Oil Recovery. SPE Textbook

## Slide 5
Is a surfactant blend a potential candidate for EOR ?
Decrease IFT between aqueous phase and crude oil.
Produce clear aqueous surfactant solutions tolerant to divalent ions (Ca2+ and Mg2+)
Alter wettability of the rock.
Transport the surfactant solution as a foam in the fractured reservoir.
Have stability at 100°C

## Slide 6
Chart: HLB
| 47.95 | 39.300000000000004 | 35.275000000000013 | 19.55 | 18.100000000000001 | 21.4 | 23.3 | 11.350000000000026 | 9.9250000000000007 | 7.55
 | 0 | 0 | 0
 | 1 | 1 | 1 | 1
 | -1 | -1 | -1
Lipophilic Hydrophilic
Using Davies approach for HLB, and calculated with tables given by Guo et al (2006)
Surfactants used in the study:
Blends of Anionic + Cationic + Zwitterionic
+
-
-
+
Surfactants for foaming blends
in seawater at 94°C

## Slide 7
Chart: HLB
| 13.9 | 7.55 | 14.870000000000006 | 7.55 | 29.43 | 8.0300000000000011 | 17.3 | 10.16
 | 1 | 1
 | 2 | 2
 | 3 | 3
 | 4 | 4
A4
A5
A6
A7
A8
A9
A10
A11
Additional surfactants studied:
Binary anionic surfactant blends
Lipophilic Hydrophilic
Using Davies approach for HLB, and calculated with tables given by Guo et al (2006)
Xiaowen Guo, Zongming Rong, Xugen Ying Calculation of hydrophile-lipophile balance for polyethoxylated surfactants by group contribution method. Journal of Colloid and Interface Science 298 (2006) 441-450
-
-

## Slide 8
Chart: 
| 0 | 50
 | 0 | 86.6025
 | 86.6025 | 0
 | 0 | 0
 | 0 | 17.3205 | 21.6506 | 28.8675 | 32.476 | 36.0844 | 43.3013 | 57.735 | 79.3857 | 86.6025 | 0 | 7.6809 | 14.5506 | 19.9478 | 0 | 17.0026 | 19.2703 | 16.8801 | 8.2292 | 7.9279 | 17.8106 | 0 | 14.4338 | 22.4525 | 25.3387 | 24.4631 | 38.7713 | 28.59 | 29.1068 | 43.3013 | 21.6506 | 64.9519 | 0 | 28.8675 | 28.8675 | 28.8675 | 28.8675
 | 100
 | 5
 | 5
 | 36.0844 | 29.1068 | 25.3387 | 17.8106 | 19.2703 | 19.9478 | 0
Solubility map at room temperature for the pseudo ternary surfactant system. 1% Overall surfactant concentration in synthetic seawater for Z2-A2-C4.
Solubility map were obtained to select the range of proportions to be studied
1% Surfactant solution in Seawater
30º C (Similar at 94ºC)
Precipitate
Precipitate
Clear
Clear solutions
+
-
-
+

## Slide 9
Foam experimental set up for high temperature

## Slide 10
Chart: Time h
 | 0 | 12
Before starting the co-injection, 0.5 PV of surfactant solution was fed. Co-injection starts at time zero. Injection was 2 cm3/min of surfactant and 20 sccm of N2. The foam quality at inlet conditions was 70%. Injection stopped after 1 h, and the system kept producing foam for additional 45 min. 1 PV of liquid injected is equivalent to 0.47 h, total superficial velocity 76 ft/day.
Surfactant: 1% A2 in NaCl brine at seawater ionic strength. (Anionic)
Typical startup of a strong foam

## Slide 11
Chart: Time, h
1, 10 | 0 | 12
Oil Inj | 0 | 12
Oil Stop | 0 | 12
The surfactant flow rate was 1 cm3/min, Nitrogen injection at 10 sccm. Oil injection was at 0.1 cm3/min for 25 min, as indicated in the figure. Total superficial velocity 38 ft/day. 55 min of injection of liquid is equivalent to 1 PV . System: 1% Z2+A2, 2:1 (w/w) in synthetic seawater . (Anionic + Zwitterionic)
Startup of foam and behavior while oil was co injected
Foams should not produce viscous emulsions in presence of oil
68.1% N2
29% Aqueous surfactant solution
2.9% Oil

## Slide 12
Foam in the presence of oil under the microscope at room temperature
Foam sampled from shaking ~10 ml of 1% solution with 1 cc of synthetic oil.
80mm
80mm
Gas
Aqueous phase
Gas
Gas
Aqueous phase
Aqueous phase
Crude oil
Crude oil
Aqueous phase
Gas
Crude oil
stuck
Lamella zoomed
80mm
80mm
Effect of oil on the with EL foam in SW, The same trend is observed for the system Zwitterionic + Anionic (2-1) foam in Sea water 94°C

## Slide 13
Chart: flow rate cm3/min
| 2.8448029840706162 | 1.4308980070816077 | 0.58386780100169156 | 0.36442221794583113 | 4.5324255438674745
LB-AOSC1618 (2-1) | 436.3136 | 790.3394 | 1606.2119 | 2391.777 | 316.4544
AOSC1618 | 260.0586 | 241.7606 | 639.0781 | 158.7139 | 454.8704 | 1523.7283 | 4877.9672
fit | 7958.005 | 5117.9471 | 3291.4509 | 2116.7958 | 1361.3524 | 875.5121 | 563.0588 | 362.114 | 232.8825 | 149.7713 | 96.3208
CTAB-NapTS (1-1) | 199.3532 | 323.2199 | 391.6531 | 443.995 | 408.6149 | 443.7115 | 326.707 | 400.0501
LB-AOSC14-BTC8358 | 152.3368 | 239.7354 | 610.9046 | 760.2758 | 330.3253 | 488.5429 | 886.0178 | 1047.2795
LB-AOSC1618-BTC8358 (13-2-1) | 457.4589 | 613.7707 | 251.6839 | 142.7423
 | 581.3069 | 426.99 | 313.6388 | 230.3785 | 169.221 | 124.2986 | 91.3016
 | 383.3036 | 281.2531 | 206.3724 | 151.4279 | 111.1118 | 81.5295 | 59.8231 | 43.8958 | 32.209
 | 350 | 420 | 475 | 469.4985 | 345.871 | 254.7969 | 187.7043 | 138.2784 | 101.8672 | 75.0437
 | 460 | 600 | 573.5609 | 422.5319 | 311.2716 | 229.3082 | 168.9272 | 124.4456 | 91.6768 | 67.5367
 | 4849.676 | 3492.0368 | 2514.4609 | 1810.5519 | 1303.6982 | 938.7353 | 675.9417 | 486.7156 | 350.4624 | 252.3524 | 181.7078 | 130.8397 | 94.2119
 | 250 | 750 | 950 | 985 | 975 | 940 | 900 | 820 | 720 | 582.6385 | 492.4455 | 416.2144 | 351.7839 | 297.3274 | 251.3008 | 212.3991 | 179.5195 | 151.7297 | 128.2418 | 108.3898 | 91.6109 | 77.4295
Comparison of foam strength for different surfactants at 94°C and 1% total surfactant concentration in a sand pack, using qualities between 60 -70%. Straight lines are for power law fit ( n ca - 0.8)
Foam Strength
Shear thinning effect

## Slide 14
Chart: Quality
| 0.64017953627484514 | 0.19306273270378788 | 0.93969109869886314 | 0.97737689296521002
 | 379.1519 | 471.1462 | 160.1219 | 39.0005
 | 0.3 | 100 | 325 | 400 | 470 | 460 | 450 | 455 | 400 | 390 | 375 | 360 | 350 | 325 | 300 | 275 | 250 | 200 | 180 | 160 | 150 | 100 | 10 | 1
Effect of gas quality on foam viscosity for 0.33% Overall blend concentration in synthetic sea water at 94°C for a constant total flow rate of 3cm3/min (34.5 ft/day of superficial velocity) H1 = Hydrotrope 1 (Na pTS)
Effect of quality in foam strength for different surfactants
Chart: Quality
| 0.60415304415671001 | 0.63060095306312114 | 0.14856345957953074 | 0.92601278836955758 | 0.93275834065341301
 | 508.8054 | 605.9096 | 408.9154 | 712.9107 | 680.0617
 | 465.095 | 307.0695 | 757.2601
 | 50 | 100 | 200 | 331.174 | 354.326 | 377.478 | 400.63 | 423.782 | 446.934 | 470.086 | 493.238 | 516.39 | 539.542 | 562.694 | 585.846 | 608.998 | 632.15 | 655.302 | 678.454 | 701.606 | 706.2364 | 713.182 | 600 | 500 | 300 | 50
Effect of foam quality on apparent viscosity for Z3+A2 and Z2 + A2 at 1% total surfactant concentration in synthetic seawater, 94°C and constant total flow rate of 2 cm3/min, superficial velocity 23 ft/day

## Slide 15
F1 | Strengthen of foam for surfactant concentration
F2 | Gas mobility change as result of water saturation (*)
F3 | Foam coalescence caused by oil saturation
F4 | Increase of foam for gas velocity (Shear thinning effect)
F5 | Shear-thinning effect in low quality regime
F6 | Critical capillary number effect
fmmob | Normalized resistance to flow of a minimum-size bubble, in the absence of factors increasing bubble size. Surguchev approach according with Rossen et al. (2003)
Components of the model in this study
Relative-permeability of gas as foam
Relative-permeability for aqueous phase
Mathematical Model, parameters fit and simulation.
The mathematical model selected was the empirical method that uses the mobility reduction factor approach. This approach at different degrees of complexity has been incorporated in simulators like UTCHEM, ECLIPSE 200, UTCOMP and STARS

## Slide 16
Chart: Foam quality
| 0.67239144958503916
0.15 cm3/min | 4698.91
0.47 cm3/min | 2089.7542 | 1819.7389 | 2236.488 | 1584.9077
0.67 cm3/min | 1430.56
1.3 cm3/min | 0 | 594.2429 | 657.9056 | 785.2412 | 859.5228 | 955.0119 | 976.2193 | 975.3089 | 954.9512
2.45 cm3/min | 461.6
0.47 | 596.1 | 946.2 | 1353 | 1449 | 1523 | 1583 | 1635 | 1679 | 1718 | 1753 | 1784 | 1812 | 1838 | 1861 | 1882 | 1901 | 1918 | 1934 | 1948 | 1961 | 1972 | 1982 | 1990 | 1997 | 2002 | 2006 | 2007 | 2007 | 2005 | 2001 | 1993 | 1983 | 1968 | 1948 | 1920 | 1883 | 1830 | 1749 | 1280 | 852.2
1.3 | 290.5 | 458.8 | 654.4 | 700.2 | 735.8 | 764.9 | 789.5 | 810.9 | 829.7 | 846.4 | 861.5 | 875.1 | 887.4 | 898.6 | 908.9 | 918.2 | 926.8 | 934.6 | 941.6 | 948 | 953.7 | 958.7 | 963.1 | 966.9 | 970 | 972.4 | 974.1 | 975 | 975 | 974 | 971.9 | 968.5 | 963.4 | 956.3 | 946.3 | 932.3 | 912.1 | 880.8 | 674 | 437.3
0.15 | 1347 | 2142 | 3063 | 3278 | 3444 | 3579 | 3693 | 3792 | 3878 | 3955 | 4023 | 4084 | 4139 | 4189 | 4233 | 4274 | 4309 | 4341 | 4369 | 4394 | 4414 | 4431 | 4444 | 4453 | 4459 | 4460 | 4456 | 4447 | 4432 | 4411 | 4382 | 4344 | 4294 | 4230 | 4146 | 4037 | 3887 | 3673 | 2628 | 1844
0.67 | 463.5 | 734.8 | 1050 | 1124 | 1182 | 1229 | 1268 | 1303 | 1333 | 1360 | 1384 | 1406 | 1426 | 1444 | 1461 | 1476 | 1489 | 1502 | 1513 | 1523 | 1532 | 1540 | 1546 | 1552 | 1556 | 1560 | 1562 | 1562 | 1561 | 1559 | 1554 | 1547 | 1537 | 1523 | 1504 | 1477 | 1439 | 1381 | 1025 | 673.9
2.45 | 186.7 | 293.4 | 417.3 | 446.2 | 468.7 | 487.1 | 502.6 | 516.1 | 527.9 | 538.5 | 547.9 | 556.5 | 564.2 | 571.3 | 577.7 | 583.6 | 589 | 593.9 | 598.3 | 602.4 | 606 | 609.2 | 612 | 614.4 | 616.4 | 618 | 619.1 | 619.8 | 620 | 619.6 | 618.6 | 616.7 | 614 | 610 | 604.5 | 596.8 | 585.6 | 568.2 | 449 | 291.2
Mobility reduction approach model, can be used to reproduce some trends of the foam behavior observed in the lab.
Parameter | Values
epdry | 56*
fmdry | 0.0823
fmmob | 17.5
epv | -0.78
Ug ref | 1.4
Comparison Results for 1% Z2+A2 (2:1)
In seawater at 120°C
Dashed and continuous lines are from the model, symbols are experimental data

## Slide 17
Chart: Total flow (cm3/min)
| 0.1 | 0.15000000000000024 | 0.27500000000000002 | 0.3375000000000114 | 0.50624999999999998 | 0.75937500000002012 | 1.1390625000000001 | 1.7085937499999628 | 2.5628906249999988 | 3.8443359374999999 | 5.7665039062499845 | 8.6497558593750004 | 12.9746337890625 | 19.461950683593749 | 29.19292602539063 | 43.789389038086 | 65.684083557128758 | 98.526125335693351
 | 59.0693 | 375.6607 | 809.2435 | 866.9031 | 866.9015 | 774.7383 | 648.218 | 521.1332 | 408.8499 | 316.0485 | 242.2183 | 184.7967 | 140.7374 | 107.1964 | 81.7707 | 62.532 | 47.9775 | 36.956
 | 152.3368 | 239.7354 | 610.9046 | 760.2758 | 330.3253 | 488.5429 | 886.0178 | 1047.2795
 | 23.8066 | 95.3417 | 282.9032 | 406.1649 | 436.9828 | 406.5542 | 348.704 | 285.0975 | 226.4811 | 176.8511 | 136.7409 | 105.1895 | 80.7631 | 62.0257 | 47.7226 | 36.8274
 | 199.3532 | 323.2199 | 391.6531 | 443.995 | 408.6149 | 443.7115 | 326.707 | 400.0501
 | 152.3368 | 239.7354 | 610.9046 | 760.2758 | 330.3253 | 488.5429 | 886.0178 | 1047.2795
Model without F5 and F6 | 6522.1722 | 4810.4633 | 3552.0268 | 2626.0962 | 1944.2159 | 1441.5755 | 1070.6651 | 796.6404 | 593.9349 | 443.7756 | 332.3701 | 249.5776 | 187.9364
LB-AOS | 465.4012 | 809.616 | 1511.7288 | 2240.3987 | 335.9285
The model can be used to reproduce the effect of minimum
velocity required to foam
Simulation of the foam viscosity using the mobility reduction factor approach. The symbols are experimental data at gas quality close to used in the simulation of 70%.
Results are consistent with observation done by Cheng et al (2000), where he establish a relationship with the shear thinning exponent and the parameter epcap
Parameter | Values
Surfactant | Z2+A2+C4
epdry | 100
fmdry | 0.08
fmmob | 17.5
epv | -0.78
Ug ref | 1.42
epcap | 3
epn | 3
Uref (m/s) | 3.3x10-6

## Slide 18
Qualitative study of transport of phases in heterogeneous porous media
Visualization of recovery of oil from matrix and transport of phases was conducted in a experimental setup that mimics fractured reservoir.
The matrix was represented with micro-channels filled with crude oil.
The fractures were represented with glass beads
The micro-channels were embedded in a packed bed of glass beads where foam was transported.
Different flow configurations were evaluated.

## Slide 19
Comparison among permeability ratios for capillaries, glass beads and reservoir rock
Section | Permeability (darcy) |  |  |  | Contrast ratio
Porous media | Fracture |  | Matrix |  | 
 | Simulated |  | Simulated |  | 
Glass beads (6 mm) | 23000 |  |  |  | 
100 mm slit |  |  | 690 |  | 33
50 mm slit |  |  | 170 |  | 135
20 mm slit |  |  | 28 |  | 821
FORMATION |  | 10 |  | 0.01 | 1000 *
* Extreme case
Chart: Permeability (Darcy)
| 1 | 1
Fracture | 10 | 1
Matrix H | 1 | 0.5
Matrix M | 0.5 | 0.3
Matrix L | 0.3 | 0.01
Permeability in the formation
Description of the formation
Matrix-Fracture
Description of the experimental
Matrix-Fracture setup

## Slide 20
Dry Foam
Wet Foam
Surfactant
(aqueous)
Nitrogen
(gas)
Sintered
Stainless steel filter
Effect of gravity on foam quality should be taken into consideration
Challenges of foam models for applications in fractured reservoirs
Use Edit mode to see the clips by Double click the icons (do not use Slide Show mode)

## Slide 21
Foam flowing upward (vertical channel)
Foam flowing horizontal (horizontal channel)
Stagnant foam and vertical micro-channel
Use Edit mode to see the clips by Double click the icons (do not use Slide Show mode)

## Slide 22
Frames from inlet section during horizontal flow
~30 Sec time interval 10 Sec
Foam Surfactant solution Oil
100 m
1000 m
Mimic of
Foam in fractures
Fractures:
Glass beads
Matrix:
Micro-channels
Effect permeability for transport of foam and components

## Slide 23
Conclusions and recommendations
about foam experiments
A systematic study of surfactant blends with the purpose of identify their foaming potential at 94°C in seawater in a silica sand pack permitted the selection of best candidates.
This study gave additional information regarding to the behavior of surfactants in presence of oil, the behavior of foam at different fractional flows and different qualities of foam.
An existing mathematical model for foams was used to verify if by fitting parameters it was possible to predict trends observed during the different experimental tests. The model was able to reproduce experiments and predict observed behavior in steady state foam flow.
Micro-channels embedded in glass beads were used for visualization of transport of phases to mimic fracture and matrix.
The physical model that mimics the matrix-fracture will give qualitative information of transport of phases to test the mathematical model in the initial stage.

## Slide 24
Acknowledgments:

## Slide 25
Grad students:
Aarthi Muthuswamy
AmirHosein Valiollahzadeh
Kun Ma
Acknowledgments:

## Slide 26: END Backup slides

## Slide 27
Polyhedral foam
High quality
Spherical bubbles
Low quality

## Slide 28
Experiment vertical T
20 mm capillary.
no bubbles of N2 are seen in the inlet of the capillary

## Slide 30
Si
Si
Si
Si
Si
Si
Si
O
O
O
O
O
O
OH
OH
OH
OH
OH
OH
Si
CH3
CH3
Cl
Cl
Si
CH3
CH3
Cl
Cl
Si
CH3
CH3
Cl
Cl
Hydrophilic
Si
Si
Si
Si
Si
Si
Si
O
O
O
O
O
O
O
O
O
O
O
O
Si
CH3
CH3
Si
CH3
CH3
Si
CH3
CH3
Si
O
6 HCl
Hydrophobic
Glass micro channels were treated to be oil-wet
Dichlorodimethylsilane

## Slide 31
Foam strength after oil production
Chart: Total flow rate cm3/min
| 0.1 | 0.2 | 0.4 | 0.8 | 1.6 | 3.2 | 6.4 | 12.8 | 19.2 | 25.6
C16-18AOS in SWIS | 7876.1274 | 4092.5115 | 2126.5083 | 1104.9541 | 574.1448 | 298.3311 | 155.0157 | 80.5477 | 54.9205 | 41.8533
Upstream | 80.5477 | 127.963 | 152.782 | 212.05 | 239.749 | 200
Downstream | 80.5477 | 147.1575 | 150 | 162.1559 | 159.7599 | 50
 | 10 | 25
Mixture of A9 and A8 in proportion 70:30 (w/w).
The green points are for the upstream section.
The orange dots are for the downstream.
Gray line is the benchmark and corresponds to 1% A2 in NaCl brine at seawater ionic strength. 1 cm3/min corresponds to 11.5 ft/day of superficial velocity.
A2 in NaCl
(Sea Water Ionic strength)

## Slide 32
Silica sand Mesh 20-40
Rubber stopper
5 1/2
Rubber stopper
Sieve
Mesh 200
Rubber stopper
Rubber stopper
5 1/2
Sieve
Mesh 200
Internal
Taps

## Slide 33
Anionic s
Zwitterionics
Cationics
A1
A2
A3
A4,A5
A6,A7
A8,A9
A10,A11
Z1
Z2
Z3
C1
C2
C3
C4

## Slide 34
Chart: Total flow rate cm3/min
| 3.9667866303152377 | 4.0844727143034927 | 1.186908352957512 | 6.9515797556199024 | 1.9404425064376187 | 0.42540126439727005 | 9.047311596515091E-2
First section | 283.7003 | 264.7211 | 697.1761 | 174.5853 | 497.5145 | 1556.148 | 4877.9672
Second section | 236.4169 | 218.8001 | 580.9801 | 142.8425 | 412.2263 | 1491.3085 | 4877.9672
fit | 7958.005 | 5117.9471 | 3291.4509 | 2116.7958 | 1361.3524 | 875.5121 | 563.0588 | 362.114 | 232.8825 | 149.7713 | 96.3208
Apparent viscosity vs. total flow rate for quality between 0.7 and 0.78 at 94°C, 1% A2 in NaCl brine at seawater ionic strength.
Shear thinning foam behavior

## Slide 35
Chart: 
| 0 | 50
 | 0 | 86.6025
 | 86.6025 | 0
 | 0 | 0
 | 0 | 17.3205 | 21.6506 | 28.8675 | 32.476 | 36.0844 | 43.3013 | 57.735 | 79.3857 | 86.6025 | 0 | 7.6809 | 14.5506 | 19.9478 | 0 | 17.0026 | 19.2703 | 16.8801 | 8.2292 | 7.9279 | 17.8106 | 0 | 14.4338 | 22.4525 | 25.3387 | 24.4631 | 38.7713 | 28.59 | 29.1068 | 43.3013 | 21.6506 | 64.9519 | 0 | 28.8675 | 28.8675 | 28.8675 | 28.8675
 | 100
 | 5
 | 5
 | 36.0844 | 29.1068 | 25.3387 | 17.8106 | 19.2703 | 19.9478 | 0
Solubility map at room temperature for the pseudo ternary surfactant system. 1% Overall surfactant concentration in synthetic seawater for Z-A-C.
Solubility map is needed to know the range of concentrations to be studied
1% Surfactant solution in Seawater
30º C (Similar at 94ºC)
Precipitate
Precipitate
Clear
Clear solutions

## Slide 36
36
Dry Foam
Wet Foam
Foam
Dry foam
Wet foam
Dry foam
Wet foam
For the glass T, foam segregates having high quality in the upper region and low quality in the lower region

## Slide 37
Rectangular capillary tube
Cross section
1000 mm x 100 mm
Apparatus for horizontal foam flow

## Slide 38
h
G.J. Hirasaki and D.L. Zhang, "Surface Chemistry of Oil Recovery from Fractured, Oil-Wet, Carbonate Formations,“
SPE Journal 151-162, 2004
Cartoon of a oil wet scenario

## Slide 39
Conditions for mobility control and
improved displacement efficiency with foam
Hypothesis of the vuggy fractured network

## Slide 40
  Alongside studies to determine what surfactants have potential for recovering oil in fractured reservoirs
Oil and foam flow in
“micro channel”
  Phase behavior
  with oil
  Wettability
  alteration
Imbibition
Amott cell
Special set up for
foam flow in reservoir rock
  Imbibition in foaming milieu
Lopez Salinas Rice University, Ph.D.Thesis 2012

## Slide 41
 | Anionic |  |  | Zwitterionic |  |  | Cationic |  |  |  | Notes |  |  | 
Test | A3 | A2 | A1 | Z2 | Z3 | Z1 | C4 | C1 | C2 | C3 | Brine | Oil | Flow | Foams
16,17 |  | x |  |  |  |  |  |  |  |  | SWIS | Y,N | ↑ &↓ | Y
24 | x |  |  | x |  |  |  |  |  |  | SW | N | ↑ & ↓ | Y
15,26 |  | x |  | x |  |  |  |  |  |  | SW | Y,N | ↑ | Y
25 |  |  | x | x |  |  |  |  |  |  | DIW | N | ↑ | Y
14 |  | x |  |  | x |  |  |  |  |  | SW | Y,N | ↑ | Y
20 |  | x |  |  |  | x |  |  |  |  | SW | N | ↑ | Y
27 |  |  |  |  | x |  |  |  |  | x | SW | N | ↑ | Y
21 |  |  |  | x |  |  | x |  |  |  | SW | N | ↑ | N
28 |  | x |  | x |  |  | x |  |  |  | SW | Y,N | ↑ | Y
29 | x |  |  | x |  |  | x |  |  |  | SW | N | ↑ | Y
13 |  |  |  |  |  |  | x |  |  |  | SW | N | ↑ | N
23 |  |  |  |  |  |  |  | x |  |  | SW | N | ↑ | N
22 |  |  |  |  |  |  |  |  | x |  | SW+ Na pTS | N | ↑ | Y
↑ flow upward
↓ Flow downward
Surfactants blends used in the study

## Slide 42
Chart: HLB
| 47.949999999999996 | 39.300000000000004 | 35.275000000000013 | 19.55 | 18.100000000000001 | 21.4 | 23.3 | 11.350000000000026 | 9.9250000000000007 | 7.55
 | 0 | 0 | 0
 | 1 | 1 | 1 | 1
 | -1 | -1 | -1
Lipophilic Hydrophilic
+
-
-
+

## Slide 43
Chart: 
| 0 | 50
 | 0 | 86.6025
 | 86.6025 | 0
 | 0 | 0
 | 0 | 17.3205 | 21.6506 | 28.8675 | 32.476 | 36.0844 | 43.3013 | 57.735 | 79.3857 | 86.6025 | 0 | 7.6809 | 14.5506 | 19.9478 | 0 | 17.0026 | 19.2703 | 16.8801 | 8.2292 | 7.9279 | 17.8106 | 0 | 14.4338 | 22.4525 | 25.3387 | 24.4631 | 38.7713 | 28.59 | 29.1068 | 43.3013 | 21.6506 | 64.9519 | 0 | 28.8675 | 28.8675 | 28.8675 | 28.8675
 | 100
 | 5
 | 5
 | 36.0844 | 29.1068 | 25.3387 | 17.8106 | 19.2703 | 19.9478 | 0
Precipitate
Precipitate
Clear
Clear solutions
+
-
-
+

## Slide 44
foam entering capillary_ in this instance at high rate,
Surfactant solution displacing the crude oil ,foam background outside capillary
Picture of capillary under the microscope after ending horizontal-foam test at different position from inlet .
1000 mm
Polyhedral or dry
foam
Wet
foam
Dragged capillary wetting oil by foam
Surfactant solution
displacing oil

## Slide 45
Equipment
Video Camera: Panasonic GP-KR222 (Industrial Color CCD Camera)
Lens:Computar Macro 10X
Micro channels
Microslides: Vitrto Dynamics Inc and VitroCom Inc.
Camera for Microscope: Minivue 3.1M (Aven, Inc.)
Microscope:
Nikon Polarizing Microscope. OPTIPHOT-POL
4p, 0.1, 160/-
TV Relay Lens 1x/16 (between microscope and camera)
200 mm x 4000 mm x 5 cm
100 mm x 1000 mm x 5 cm
50 mm x 500 mm x 5 cm
20 mm x 200 mm x 5 cm

## Slide 46
Equipment
Oven: Associated Environmental Systems to control temperature 94°C
Foam pre generator packed with Glass Microspheres
380-515 mm
Duke Scientific Corp.
Glass beads to mimic fractures
Fisher Scientific 6mm Glass beads Solid
Liquid pump: Syringe ISCO Series D, 260D
Gas Flow Controller: Matheson M8270
Additional: Swagelok fittings, 1/16 in stainless steel tubing, 1/16 in teflon tubings, Rubber stoppers, Stands, Clamps, Glass syringe, 1/16 SS bold needle, etc.

## Slide 47
Conclusions and recommendations
about foam experiments
The experimental setup built to study foam under harsh conditions permitted collection of data with minimum noise or oscillation in the back pressure (±0.2psi)
A systematic study of surfactant blends with the purpose of identify their foaming potential at 94°C in seawater in a silica sand pack permitted the selection of best candidates.
This study gave additional information regarding to the behavior of surfactants in presence of oil, the behavior of foam at different fractional flows and different qualities of foam.
An existing mathematical model for foams was used to verify if by fitting parameters it was possible to predict trends observed during the different experimental tests. The model was able to reproduce experiments and predict observed behavior in steady state foam flow. However, non-uniqueness of the parameters seems possible. Tuning of parameters will require additional foam tests at transient conditions.