## Slide 1: CO2 Mobility Control in Carbonate Cores
Consortium Meeting Apr. 29th 2013
Presented by Leyu Cui
Kun Ma, Ramesh Pudasaini, Maura Puerto and George Hirasaki
Sponsored by ADNOC and DOE

## Slide 2: Outline
Setup Diagrams
Surfactants and Cores
C12/DI and CO2 foam
C12/Brine and CO2 foam
Conclusion

## Slide 3: Outline
Setup Diagrams
Surfactants and Cores
C12/DI and CO2 foam
C12/Brine and CO2 foam
Conclusion

## Slide 4: Diagram of the high temperature and high pressure core flooding setup
Pumps System
All wetting materials are Hastelloy Alloys, which can work under high P, T, salinity and low pH.

## Slide 5: Pumps system and Core Holder Module

## Slide 6: Pressure Transducer Module

## Slide 7: BPR Module

## Slide 8
3400 psi, 82 ˚C (180 ˚F)
Joule-Thomson Expansion
1200 psi, 35 ˚C
1200 psi, 82 ˚C
14 .5psi, 15 ˚C
Joule-Thomson Expansion
Isobaric Heating
Carbon Dioxide: Pressure-Enthalpy Diagram
*Good plant design and operation for onshore carbon capture installations and onshore pipelines, Energy Institute, 2010 09,

## Slide 9: Outline
Setup Diagrams
Surfactants and Cores
C12/DI and CO2 foam
C12/Brine and CO2 foam
Conclusion

## Slide 10: Surfactant and Brine
C12: ethoxylated amine from AKZO NOBEL Co. is dissolved in DI water. C12’s molecular weight is 288 g/mol.
R = Coco group (≈ 8 to 16 carbon)
x + y=2
Brine: 22% TDS (total disolved solids) with high divalent ions (Ca2+, Mg2+) concentrations.

## Slide 11: Silurian Dolomite Core
Diameter=1.5 in.
Length= 7.6 cm= 2.99 in.
Permeability is 737 md, measured by water
Chart: Superficial Velosity ft/day
| 8.2877770429683988 | 16.575554085936787 | 24.863331128905219
 | 2.0053 | 3.6295 | 5.2337

## Slide 12: Outline
Setup Diagrams
Surfactants and Cores
C12/DI and CO2 foam
C12/Brine and CO2 foam
Conclusion

## Slide 13: Injection Procedure: a slug of CO2 is injected before C12
Chart: pH, at room temperature
| 4 | 4 | 4 | 4 | 4 | 4 | 4
Clear | 22 | 50 | 70 | 90 | 110 | 120 | 130
Hazy | 22 | 50 | 70 | 90 | 110 | 120 | 130
Cloudy | 22 | 50 | 70 | 90 | 110 | 120 | 130
1% C12 in DI Water
pH is adjusted by acetic acid
WAG is injected to acidify the core to pH <4 before C12 and CO2 co-injection.
Both WAG and Co-injection have the same foam quality.
Chart: pH
| without CO2 | 3400 psi CO2
 | 9.9 | 3.9
pH of water equilibrium with Dolomite

## Slide 14: C12 Plug the Core without CO2
Chart: PV
 | 0 | 1500
C12/DI is saturated with CO2 under 1 atm. The pH is decreased to 5 to dissolved C12 in water at room temperature.

## Slide 15: Normalized Pressure Gradient: Apparent Viscosity
Apparent viscosity is used to describe the foam strength, which is calculated by Darcy’s law:
where is foam apparent viscosity, is core permeability, is the total superficial velocity and is the pressure gradient.

## Slide 16: C12/DI and CO2 Foam Pressure History at 20 °C and 3400 psi
Chart: TPV
30% Foam Quality
Chart: TPV
50% Foam Quality
Chart: TPV
70% Foam Quality
Chart: TPV
80% Foam Quality
µ*=78.91 cp
µ*=118.30 cp
µ*=139.98 cp
µ*=65.72 cp

## Slide 17: Experimental Data vs. Foam Model for C12/DI and CO2 foam
krw0=0.5; krg0=0.1768; S_wc=0.33; S_gr=0.2; nw=2.8; ng=1.1; (Bennion, 2008)
µw=1 cp; µg=0.1025 cp;
epdry=200; fmmob=340.99; fmdry=0.39;
(Rossen, W. R. and Renkema, W. J. (2007); Ma, K., Lopez-Salinas, J.L and et al., Energy & Fuels (in press).)

## Slide 18: Outline
Setup Diagrams
Surfactants and Cores
C12/DI and CO2 foam
C12/Brine and CO2 foam
Conclusion

## Slide 19: C12/Brine and CO2 Foam Pressure History at 20 °C and 3400 psi
Chart: TPV
Chart: TPV
30% Foam Quality
50% Foam Quality
Chart: TPV
70% Foam Quality
Chart: TPV
80% Foam Quality

## Slide 20: Salt may precipitate at high foam quality
Chart: PV
discontinued point 1 | 1 | 1000
discontinued point 2 | 1 | 1000
discontinued point 3 | 1 | 1000
Chart: PV
Discontinued Point 1 | 1 | 1000
Discontinued point 2 | 1 | 1000
Discontinued point 3 | 1 | 1000
90% Foam Quality
90% Foam Quality
Nadja Mullera, Ran Qib, and et al., CO2 injection impairment due to halite precipitation, Energy Procedia, Volume 1, Issue 1, 2009
S. Hurter, D. Labregere, and J. Berge, Simulations for CO2 injection projects with Compositional Simulator, SPE 108540, 2007
Average apparent viscosity

## Slide 21: Experimental data vs. Foam model for C12/Brine and CO2 foam
krw0=0.5; krg0=0.1768; S_wc=0.33; S_gr=0.2; nw=2.8; ng=1.1; (Bennion, 2008)
µw=1 cp; µg=0.1025 cp;
epdry=10000; fmmob= 549.35; fmdry= 0.37;
(Rossen, W. R. and Renkema, W. J. (2007). )

## Slide 22: Comparison of Foam in DI water and brine at room temp.

## Slide 23: C12/Brine and CO2 Foam at 120 °C and 3400 psi
60% Foam Quality
Chart: TPV
MPG | 10 | 10
Chart: TPV
MPG | 10 | 10
µ*=59.14 cp

## Slide 24: Comparison of viscosity at 20 and 120 °C for C12/Brine and CO2 Foam
krw0=0.5; krg0=0.1768; S_wc=0.33; S_gr=0.2; nw=2.8; ng=1.1; (Bennion, 2008)
µw=0.2381 cp; µg=3.935×10-2 cp;
epdry=10000

## Slide 25: Conclusion
The cloud point of C12 is lower than room temperature at pH>9. A slug of CO2 should be injected before C12 solution in carbonate reservoir.
C12 can generate strong foam in a wide range of foam quality. But foam generation is delayed at high foam quality, because the surfactant solution is diluted by residual water.
The foam is stronger in brine than in DI water for C12 and CO2 foam. The foam strength is reduced at elevated temperature.
The local equilibrium model can fit our experimental data. But this foam model doesn’t include capillary force, solubility factor, et al. which probably caused the difference between the experimental data and calculation result.

## Slide 26: Questions?
Thank you!

## Slide 27: Back Up

## Slide 28: Water saturation doesn’t change too much during WAG

## Slide 29: Close to connate water saturation (Swc) at high foam quality

## Slide 30
ESEM photograph of Berea sandstone after 32 hrs of CO2 flooding. Red arrows point at Hopper NaCl crystals. (Nadja Mullera, Ran Qib, and et al., CO2 injection impairment due to halite precipitation, Energy Procedia, Volume 1, Issue 1, 2009)

## Slide 31: Water evaporation to CO2
N. Spycher, K Pruess, J Ennis-King, CO2- H2O mixtures in the geological sequestration of CO2. I. Assessment and calculation of mutual solubilities from 12 to 100C and up to 600 bar,
Geochimica et Cosmochimica Acta, 67 (16) (2003), pp. 3015–3031
yH2O: mole fraction of H2O in CO2 phase. 0.38% at 20 ˚C and 234 bar.
Convert to volumetric fraction=0.15% .
TDS increase from 22% to (22%*0.1)/(0.1-0.9*0.15%)=22.3% for 90% foam quality.
The increase of total TDS is negligible. But the local CO2 concentration is probably high and results in the high water evaporation.

## Slide 32: Step Reduce of BPR to Reach MPG
Chart: TPV
reduce BPR to increase pressure drop | 0 | 100
MPG | 10 | 10

## Slide 33: Increase the flow rate to reach the MPG
Chart: TPV
Discontinued point 1 | 0 | 100
Discontinued point 2 | 0 | 100
Discontinued point 3 | 0 | 100
Chart: TPV
MPG | 10 | 10
Discontinued point 1 | 0 | 100
Discontinued point 2 | 0 | 100
Discontinued point 3 | 0 | 100

## Slide 34: MPG vs. MSV (minimum superficial velocity)
Chart: TPV
Co-injection at 16 ft/day | 0.1288 | 1.0985 | 1.4389 | 1.4757 | 1.4904 | 1.4297 | 1.3138 | 1.334 | 1.3929 | 1.3929 | 1.4095 | 1.38 | 1.4518 | 0.89978
Co-injection at 16 ft/day | -0.29685 | 0.56964 | 0.22064 | 2.7479 | -0.2768 | 3.2092 | 0.22465 | 3.2815 | 2.1943 | 5.2311 | 3.6666 | 3.4098 | 5.4718 | 5.0385 | 5.4838 | 5.1508 | 4.0958 | 8.4082 | 27.1863 | 18.1483 | 10.402
Chart: TPV
Co-injection at 16 ft/day | -0.24069 | 1.8734 | 2.6155 | 2.6958 | 2.7279 | 2.5955 | 2.3427 | 2.3869 | 2.5152 | 2.5152 | 2.5513 | 2.4872 | 2.6436 | 1.4401
Co-injection at 16 ft/day | 0.10304 | 0.50049 | 0.34041 | 1.4996 | 0.11224 | 1.7112 | 0.34225 | 1.7444 | 1.2457 | 2.6386 | 1.921 | 1.8032 | 2.749 | 2.5503 | 2.7545 | 2.6018 | 2.1179 | 4.0959 | 12.7091 | 8.5635 | 5.0104
MPG | 10 | 10

## Slide 35: Injection Strategy: start at high flow rate to reach the MPG
Chart: TPV
Co-injection at 16 ft/day | 0.74337 | 1.8235 | 1.91 | 2.2798 | 2.8392 | 2.9753 | 3.0195 | 3.1557 | 3.1281 | 3.1538 | 3.1722 | 3.1465 | 3.2458 | 3.3912 | 3.2734 | 3.2973 | 3.4206 | 3.4666 | 3.5881 | 3.4372 | 3.474 | 3.4648 | 3.4225 | 3.566 | 3.669 | 3.5145 | 3.5365 | 3.6193 | 3.5954 | 3.612 | 3.6543 | 3.7886 | 3.152 | 2.4307 | 2.3681 | 3.1814 | 3.3084 | 3.1428 | 3.8383 | 4.3186 | 4.8301 | 5.1079 | 5.1723 | 5.8605 | 4.6774
Discontinued point | 0 | 100
Chart: TPV
Co-injection at 16 ft/day | 1.4201 | 3.7749 | 3.9634 | 4.7697 | 5.9892 | 6.2861 | 6.3824 | 6.6792 | 6.6191 | 6.6752 | 6.7153 | 6.6592 | 6.8758 | 7.1927 | 6.936 | 6.9881 | 7.2569 | 7.3572 | 7.622 | 7.293 | 7.3732 | 7.3532 | 7.2609 | 7.5738 | 7.7985 | 7.4615 | 7.5096 | 7.6901 | 7.638 | 7.6741 | 7.7664 | 8.0592 | 6.6712 | 5.0987 | 4.9623 | 6.7354 | 7.0122 | 6.6512 | 8.1675 | 9.2145 | 10.3297 | 10.9355 | 11.0759 | 12.5762 | 9.9968
MPG | 10 | 10
Discontinued point | 0 | 100