## Slide 1: Property Scaling Relations for Nonpolar Hydrocarbons
Sai R. Panuganti1, Francisco M. Vargas1, 2,
Walter G. Chapman1
1 Chemical and Biomolecular Engineering Department, Rice University, Houston, USA
2 Department of Chemical Engineering, The Petroleum Institute,
Abu Dhabi, UAE
February, 2013

## Slide 2: Outline
One-Third Rule
Electronic polarizability
Dielectric constant
Critical temperature and pressure
Surface tension
Conclusion

## Slide 3: One-Third Rule
Specific Refractivity: independent of the temperature and pressure
n, refractive index and ρ, mass density (g/cc)
For nonpolar hydrocarbons and their mixtures
Constant
True volume of the molecules in unit volume
True density of the molecules
But strictly speaking, it is a function of the mass density and can be expressed as
L-L Expansion

## Slide 4: One-Third Rule
Increase
Temperature
V increases, ρ decreases
n increases
Volume occupied by molecules without considering space between molecules
Vargas FM, Chapman WG; Fluid Phase Equilibria, 2010; 290:103-108
For nonpolar hydrocarbons

## Slide 5: Electronic Polarizability
Lorentz–Lorenz equation:
where, N – Number of molecules per unit volume
α – Polarizability
Refractive index and Polarizability are independent of the amount of material
where, Na – Avogadro number
v – Molar Volume (v = MW/ρ)
With the help of One-Third Rule the above expression simplifies as
The above equation is independent of the state of the substance and its polarizability can be computed by just knowing the molecular weight

## Slide 6: Predicted Polarizability
Chart: Mean Electronic Polarizability (cm3 x 10-24)
X=Y | 0 | 10 | 20 | 30 | 40 | 50 | 60
 | 0 | 9.6 | 19.2 | 28.8 | 38.4 | 48 | 57.6
 | 0 | 10.4 | 20.8 | 31.2 | 41.6 | 52 | 62.4
Data shown is for 80 different nonpolar
hydrocarbons belonging to different homologues series
Chart: Mean Electronic Polarizability (cm3 x 10-24)
X=Y | 0 | 10 | 20 | 30 | 40 | 50 | 60
 | 0 | 9.75 | 19.5 | 29.25 | 39 | 48.75 | 58.5
 | 0 | 10.25 | 20.5 | 30.75 | 41 | 51.25 | 61.5
Using One-Third Rule
Average absolute deviation is 4.16 %
Using Lorentz-Lorenz Expansion
Average absolute deviation is 2.72 %

## Slide 7: Dielectric Constant
It is well established that for weakly magnetic materials
εr , relative permitivity
For low-loss materials like nonpolar hydrocarbons,
k, dielectric constant
Substituting dielectric constant in the One-Third Rule and solving for dielectric constant
The dielectric constant expression can handle operational variations in temperature and pressure
It is independent of the knowledge of individual constituents of a mixture or the composition allowing the use for complex fluids such as crude oils and polydisperse polymers

## Slide 8: Predicted Dielectric Constant
Chart: Dielectric Constant
 | 2.5918 | 2.3062 | 2.3373 | 2.3394 | 2.3689 | 2.3711 | 2.4226 | 2.2857
 | 2.1899 | 2.223 | 2.2505 | 2.2522
 | 2.1948 | 2.2293 | 2.2581 | 2.1247 | 2.1623 | 2.1963 | 2.2231 | 2.2503 | 2.112 | 2.1549 | 2.1886 | 2.2094 | 2.2344 | 2.2677 | 1.7756 | 1.7931 | 1.8092 | 1.824 | 1.8378 | 1.8506 | 1.8625 | 1.8737 | 1.8841 | 1.8939 | 1.9032
 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3
 | 0 | 0.49 | 0.98 | 1.47 | 1.96 | 2.45 | 2.94
 | 0 | 0.51 | 1.02 | 1.53 | 2.04 | 2.55 | 3.06
Data shown is for 260 nonpolar hydrocarbons, including polymers, mixtures with varying temperatures and pressures
Panuganti SR, Vargas FM, Chapman WG; IEEE Transactions on Dielectrics and Electrical Insulation, 2013; Submitted
Chart: Dielectric Constant
 | 2.207 | 2.241 | 2.2698 | 2.2716
 | 2.677 | 2.3297 | 2.3641 | 2.3665 | 2.3999 | 2.4023 | 2.4625 | 2.3074
 | 2.212 | 2.2476 | 2.2778 | 2.142 | 2.1792 | 2.2136 | 2.2411 | 2.2696 | 2.1296 | 2.1718 | 2.2057 | 2.227 | 2.2528 | 2.2881 | 1.8244 | 1.8396 | 1.8536 | 1.8666 | 1.8786 | 1.8898 | 1.9003 | 1.9101 | 1.9194 | 1.9281 | 1.9363
 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3
 | 0 | 0.495 | 0.99 | 1.485 | 1.98 | 2.475 | 2.97
 | 0 | 0.505 | 1.01 | 1.515 | 2.02 | 2.525 | 3.03
Using One-Third Rule
Average absolute deviation is 1.98 %
Using Lorentz-Lorenz Expansion
Average absolute deviation is 1.0 %

## Slide 9: Critical Temperature and Pressure
From literature we have,
Thus, the following expression holds good
Applying One-Third Rule
also
Hildebrand and Scott
Buckley et al.
Let,
Hildebrand JH, Scott RL; The Solubility of Nonelectrolytes, 1950
Buckley et al; Petroleum Science and Technology, 1998; 16:251-285

## Slide 10: Critical Temperature and Pressure
Chart: f(MW,ρ20)
Chart: f(MW,ρ20)
Panuganti SR, Vargas FM, Chapman WG; Industrial and Engineering Chemistry Research, 2013; Accepted

## Slide 11: Predicting Critical Properties
Chart: Critical Temperature (K)
X = Y | 0 | 1000
Chart: Critical Pressure (atm)
X = Y | 0 | 100
Average absolute deviation
is 2.2 %
Average absolute deviation
is 4.5 %
Data shown is for 80 different nonpolar
hydrocarbons belonging to different homologues series. The applicability to mixtures is limited to nonpolar hydrocarbons composed of similar sized molecules

## Slide 12: Surface Tension from Hole Theory
Volume of hole = Volume of liquid - Volume of solid
Heat of fusion = Energy required for the formation of all the holes
Solving the Schrodinger wave equation for a hole in a liquid,
Using the correlation of a/v2 from the previous section, at a given temperature we have
For example at 20oC we have
where,
Furth R; Proc. Phys. Soc., 1940; 52:768-769
Auluck FC, Rai RN; Journal of Chemical Physics, 1944; 12:321-322

## Slide 13: Predicted Surface Tension
Average absolute deviation is 1.8 %
The practical application of equation can improved further by incorporating the temperature variation of surface tension
With reference temperature as 20°C, surface tension at any other temperature can be calculated as
The parameter of critical temperature can be eliminated using the equation obtained in the critical properties section.
Chart: Experiment
| 30.130000000000031 | 29.02 | 27.919999999999987 | 26.810000000000031 | 25.71 | 24.610000000000031 | 23.5 | 22.4 | 21.29 | 20.190000000000001
n-Xylene | 30.7647 | 29.4738 | 28.1756 | 26.894 | 25.6364 | 24.4001 | 23.189 | 22.0009 | 20.837 | 19.6938
Ethylbenzene | 30.641 | 29.6347 | 28.2976 | 26.9906 | 25.709 | 24.4485 | 23.2155 | 22.006 | 20.8194 | 19.6573
Methylcyclohexane | 24.19 | 22.9291 | 21.7159 | 20.5278 | 19.3679 | 18.2376 | 17.1282 | 16.0491 | 14.9969
Cyclopentane | 25.0181 | 24.3073 | 22.9187 | 21.4093 | 19.9546 | 18.5656
n-Hexane | 32.9013 | 32.4638 | 31.4695 | 30.2419 | 28.2866 | 24.2012 | 20.9681 | 19.3485 | 18.5071 | 16.2635 | 12.2106 | 8.9548 | 7.544 | 3.8505 | 2.7002 | 0.77499
 | 0 | 10 | 20 | 30 | 40

## Slide 14: Conclusion
 | Input Parameters |  |  |  | 
Property | Density | MW | Boiling Point | Function of Temperature | Mixtures
Critical Temperature | Y | Y | Y | - | Y
Critical Pressure | Y | Y | Y | - | Y
Surface Tension | Y | Y | Y | Y | N
Electronic Polarizability | N | Y | N | - | -
Dielectric Constant | Y | N | N | Y | Y
Polarizability of an asphaltene molecule of molecular weight 750 g/mol will be 99.16x10-24 cc
Polydispere asphaltene system with density between 1.1 to 1.2 g/cc at ambient conditions will have a dielectric constant between 2.737 and 3
Panuganti SR, Vargas FM, Chapman WG; IEEE Transactions on Dielectrics and Electrical Insulation, 2013; Submitted
Panuganti SR, Vargas FM, Chapman WG; Industrial and Engineering Chemistry Research, 2013; Accepted