## Slide 1: Improved Absorbents for CO2 Capture Influence of the Alkanolamine Solvent
Sumedh Warudkar
PhD Candidate (Defended)
Chemical and Biomolecular Engineering
17th Annual Meeting of the Consortium for Processes in Porous Media
Rice University, Houston, TX
April 29th, 2013

## Slide 2: CO2 and Climate Change
Chart: Year
Atmospheric CO2 variation and global temperature anomaly [Ref: 1,2,3]

## Slide 3: Carbon Capture and Storage
Schematic representation of Carbon Capture and Storage [Ref: 4]

## Slide 4: Amine Absorption Process Application: Carbon Capture
Schematic of the amine absorption process applied for post-combustion carbon capture [Ref: 5]
Feed: Flue gas
Pressure: 1 – 1.5 atm
Stripper Pressure: 1.5 – 2 atm
Temperature: 110oC – 125oC
Steam: 4 – 4.5 atm

## Slide 5: Alkanolamine Absorbents
Monoethanolamine (MEA)
Advantage
Low molecular weight
High reaction rate with CO2
Low amine circulation rate
Drawbacks
High heat of reaction
MEA concentrations above 30 wt% and CO2 loadings above 0.40 moles-CO2/mole-amine are corrosive
High volatility
Diglycolamine (DGA)
Advantage
High DGA concentrations around 50 – 70 wt% can be used due to low volatility
High reaction rate with CO2
Low amine circulation rate
Drawbacks
High heat of reaction
CO2 loadings above 0.4 moles-CO2/mole-amine are highly corrosive
Diethanolamine (DEA)
Advantage
Low volatility
Low heat of reaction
Drawbacks
High amine circulation rate
Secondary amine, low reaction rate
DEA concentrations above 40 wt% are corrosive
CO2 loadings above 0.4 moles-CO2/mole-amine are highly corrosive
A qualitative comparison of various commercial alkanolamines [Ref: 6]

## Slide 6: Amine – CO2 Reaction Monoethanolamine – A Representative Case
Ionization of Water
Dissociation of Carbon Dioxide (CO2)
Reaction of Monoethanolamine with CO2
Reaction of Monoethanolamine Carbamate with a base (amine)
Overall Reaction of Monoethanolamine with CO2

## Slide 7: Dissecting the Reboiler Energy Duty Methodology and Assumptions
Reboiler Duty
Sensible heating
Energy required to raise the temperature of the rich amine solution (~100oC) to that in the desorber (110oC - 115oC)
Heat of reaction
Energy required to reverse the endothermic reaction between alkanolamines and CO2
Generating the stripping vapor
Energy required to produce stripping vapor (mostly steam) that transports the energy for the above two processes and to dilute the CO2 released in the desorber column
Estimating these contributions
Sensible heating
Assumption: Amine flow-rate and properties remain constant in the stripper
Heat of reaction
Assumption: Heat of reaction is independent of temperature and CO2 loading of amine
Generating the stripping vapor
Assumption: All stripping vapor gets condensed in the partial condenser

## Slide 8: Dissecting the Reboiler Energy Duty Contributions of physical processes
Chart: 
| Stripping vapor duty | Heat of reaction duty | Sensible heating duty
 | 31.2047 | 33.5645 | 35.2309
Contribution of constituent physical processes to reboiler energy duty – A representative case (DEA 40 wt%, 150 kPa) [Ref: 7]

## Slide 9: Current Research on Developing Novel Absorbents
University of Texas at Austin
  Piperazine promoted Potassium Carbonate (PZ/K2CO3)
  Concentrated Piperazine (PZ)
Alstom
  Chilled Ammonia Process
Mitsubishi Heavy Industries
  Hindered amines (KS-1, KS-2)
Influences
Heat of reaction
Sensible heating
Influences
Stripping vapor
Sensible heating

## Slide 10: Why Water? A comparison of the Heat of Vaporization and Specific Heat Capacity
Chart: Co-solvent
| Water | Methanol | Ethanol | 1-Propanol | 2-Propanol | 1-Butanol | 2-Butanol | iso-Butanol | tert-Butanol
 | 2256.453 | 1098.9388 | 836.9872 | 695.8403 | 663.0616 | 584.0529 | 550.4587 | 563.9504 | 527.1182
Chart: Co-solvent
| Water | Methanol | Ethanol | 1-Propanol | 2-Propanol | 1-Butanol | 2-Butanol | iso-Butanol | tert-Butanol
 | 4.2 | 2.5044 | 2.4398 | 2.3329 | 2.5624 | 2.3861 | 2.6592 | 2.5013 | 2.9057
Comparison of specific heat capacity and heat of vaporization of water and various alcohols [Ref: 8]

## Slide 11: Vapor-liquid Equilibrium Effect of Methanol Addition
Rich Amine Loadings
Moles-CO2/mole-amine
Comparison of vapor liquid equilibrium for aqueous diethanolamine – with and without methanol [Ref: 9, 10]
Chart: CO2 Loading (α, moles-CO2/mole-amine)
| 0.05 | 0.1 | 0.15000000000000002 | 0.2 | 0.25 | 0.3 | 0.35 | 0.39999999999999997 | 0.44999999999999996 | 0.49999999999999994
DEA-Aq (35.8:64.2 - wt%) | 3.0397 | 5.8803 | 10.4733 | 17.9191 | 29.1891 | 45.7363 | 69.9973 | 105.7834 | 158.5621 | 235.628
DEA-Aq-MeOH (40:40:20 - wt%) | 2.5192 | 27.1824 | 48.9816 | 72.0202 | 112.6997 | 188.1329 | 309.7816 | 482.3206 | 707.7268 | 994.5938
Lean Amine Loadings
Moles-CO2/mole-amine

## Slide 12: Approaches to Modeling Amine Absorption
Requires extensive thermodynamic data – reaction kinetics, vapor liquid equilibria and heats of mixing.
Commercial Process Simulators
Evaluating Reboiler Duty for Alcohol blended Alkanolamines
A graphic representation of the reaction kinetics and thermodynamic complexity of models used for describing reactive absorption processes [Ref: 11]

## Slide 13: Estimating Reboiler Duty Validating the “Equilibrium Assumption”
Chart: Stripper Pressure (kPa)
| 150 | 200
Aq-DEA (35:65 - wt%) - Equilibrium Approach | 3.7 | 3.65
Aq-DEA (35:65 - wt%) - ProMax | 3.64 | 3.4
1.6%
6%
A comparison between the reboiler heat duty evaluated using the “equilibrium approach” and ProMax [Ref: 12]

## Slide 14: Reboiler Duty Effect of Methanol Addition
Chart: Reboiler Duty (GJ/ton-CO2 separated)
| Aq-DEA (60:40 - wt%) - 150 kPa | Aq-DEA-MeOH (40:40:20 - wt%) - 150 kPa | Aq-DEA (60:40 - wt%) - 200 kPa | Aq-DEA-MeOH (40:40:20 - wt%) - 200 kPa
 | 3.423 | 2.82 | 3.2412 | 2.7088
18%
17%
Effect of addition of methanol to aqueous diethanolamine on reboiler duty [Ref: 12]

## Slide 15: Reboiler Operating Temperature Effect of Methanol Addition
Chart: Reboiler Temperature (oC)
| Aq-DEA (60:40 - wt%) - 150 kPa | Aq-DEA-MeOH (40:40:20 - wt%) - 150 kPa | Aq-DEA (60:40 - wt%) - 200 kPa | Aq-DEA-MeOH (40:40:20 - wt%) - 200 kPa
 | 110.5891 | 92.8 | 116.7654 | 100.8
Effect of addition of methanol to aqueous diethanolamine on reboiler temperature [Ref: 12]

## Slide 16: Estimated Parasitic Power Loss
Chart: Parasitic Power Loss (% of Rated Power Plant Capacity)
| Aq-DEA (60:40 - wt%)-75 kPa | Aq-DEA (60:40 - wt%)-150 kPa | Aq-MeOH-DEA (40:20:40 wt%)-150 kPa | Aq-DEA (60:40 - wt%)-200 kPa | Aq-MeOH-DEA (40:20:40 wt%)-200 kPa
 | 22.078 | 37.1839 | 19.8309 | 35.5776 | 33.3187
Can Utilize Waste Heat at 20 psia, 140oC
Can Utilize Waste Heat at 20 psia, 140oC
Effect of addition of methanol to aqueous diethanolamine on the estimated parasitic power loss [Ref: 12]

## Slide 17: Solvent Polarity
Dielectric constants for water, methanol and ethanol [Ref: 8]
Chart: Solvent
| Water | Methanol | Ethanol
Dielectric Constant | 80 | 33 | 24.55

## Slide 18: CO2 Removal Studies Effect of alcohol addition
Experimental setup developed to screen the CO2 removal performance of different absorbent blends [Ref: 12]

## Slide 19: CO2 Removal Experiments
Degree of CO2 removal for 30 wt% DGA in different solvents – water, methanol and ethanol. Absorbent flow-rate: 0.02 LPM, Gas flow-rate: 3 SLPM, CO2 content: 13% (v/V) [Ref: 12]
Chart: Solvent
| Water | Methanol | Ethanol
% CO2 Removal | 71.2821 | 98.5298 | 91.123

## Slide 20: How soluble is CO2 in alcohols?
CO2 solubility in water, methanol and ethanol [Ref: 13, 14, 15]
Chart: Solvent
| Water | Methanol | Ethanol
CO2 Solubility | 1.5 | 7.7 | 6.16

## Slide 21: Kinematic viscosity of DGA solutions In Water, Methanol and Ethanol
Kinematic viscosity for 30 wt% DGA solutions in various solvents – water, methanol and ethanol
Chart: Solvent
| Water | Methanol | Ethanol
Kinematic Viscosity | 2.349 | 1.0022 | 2.0472

## Slide 22: Summary
My Hypothesis
Addition of a co-solvent to conventional absorbents such as aqueous alkanolamines can result in reduction in parasitic power loss.
Findings
A proof-of-concept case was developed using published vapor-liquid equilibrium data for methanol blended aqueous diethanolamine (DEA) (DEA:Aq:MeOH::40:40:20 wt%).
Addition of methanol to aqueous diethanolamine (DEA) resulted in a significant increase in the equilibrium partial pressure of CO2.
Reboiler duty for the methanol blended diethanolamine (DEA) system was estimated by adopting an equilibrium approach at 150 kPa and 200 kPa. Addition of methanol reduced the reboiler duty by ~18% as compared to that for aqueous diethanolamine (DEA).
Addition of methanol resulted in a decrease in the stripper/reboiler operating temperature by ~15oC. As a result, a 150 kPa stripper utilizing the methanol blended diethanolamine (DEA) can utilize waste heat.
As compared to aqueous diglycolamine, methanolic and ethanolic solutions of 30 wt% diglycolamine (DGA) appeared to increase the CO2 removal in bench-scale studies. It is believed that this is a result of higher CO2 solubility in alcohols than in water.

## Slide 23: Acknowledgements
Personnel
Dr. George Hirasaki, AJ Hartsook Professor in Chemical Engineering, Rice U.
Dr. Michael Wong, Professor in Chemical Engineering and Chemistry, Rice U.
Dr. Kenneth Cox, Professor-in-the-Practice, Chemical Engineering, Rice U.
Dr. Joe Powell, Chief Scientist at Shell Oil Company
Members of the Hirasaki and Wong research groups
Funding and Material Support
US Department of Energy (DE-FE0007531)
Rice Consortium on Processes in Porous Media
Schlumberger Ltd.
Huntsman Corporation

## Slide 24: References
National Oceanographic and Atmospheric Administration
A. Neftel, et al. “Historical carbon dioxide record from the Siple Station ice core”, Carbon dioxide Information Analysis Center (1994)
JM Barnola et al., “Historical carbon dioxide record from Vostok ice core”, Nature (1987)
Scottish Center for Carbon Storage
Image Courtesy: http://www.co2crc.com.au/aboutccs/cap_absorption.html
A.L. Kohl and R. Nielsen, Gas Purification, Gulf Publishing Company (1997)
S Warudkar, et al., Influence of stripper operating parameters on the performance of amine absorption systems for post-combustion carbon capture: Part I. High pressure strippers, International Journal of Greenhouse Gas Control (2013)
D. Green, et al., Perry’s Chemical Engineers’ Handbook. McGraw-Hill Publications (2007)
M. Z. Haji-Sulaiman, et al. Analysis of equilibrium data of CO2 in aqueous solutions of diethanolamine (DEA), methyldiethanolamine (MDEA) and their mixtures using the modified Kent-Eisenberg Model, TransIChemE (1998)
K.N. Habchi Tounsi, et al., Measurement of carbon dioxide solubility in a solution of diethanolamine (DEA) mixed with methanol, Ind. Eng. Chem. Res (2005)
E.Y. Kenig, et al., Reactive absorption: Optimal process design via optimal modeling, Chemical Engineering Science (2001)
S Warudkar, et al., “Effect of various co-solvents on the energy consumption for carbon capture” (In preparation)
I. Dalmolin, et al., Solubility of carbon dioxide in binary and ternary mixtures with ethanol and water, Fluid Phase Equilibria (2006)
K. Suzuki, et al., Isothermal vapor-liquid equilibrium data for binary systems at high pressures: carbon dioxide-methanol, carbon dioxide-ethanol, carbon dioxide-1-propanol, methane-ethanol, methane-1-propanol, ethane-ethanol, and ethane-1-propanol systems, J. Chem. Eng. Data (1990)
Image Courtesy: http://www.diytrade.com/china/pd/7727866/Silicon_carbide_ceramic_foam_filter.html