## Slide 1: Application of Asphaltene Deposition Tool (ADEPT) Simulator to Field Cases
Yi Chen, Anju Kurup, Walter Chapman
Houston, April 29 2013
Department of Chemical & Biomolecular Engineering, Rice University

## Slide 2: Outline
Introduction
Asphaltene deposition issue
The ADEPT simulator and application procedure
Field case studies
Summary

## Slide 3: Asphaltene issue in flow assurance
Flow Assurance Prediction – Operator’s Savings:
  Intervention cost to remove solids: ~ 300K/well-dry tree, $3,500K / well – wet tree.
  Loosing the well: ~ $50,000K to replace the well with a side track.
  Losses due to downtime: ~ $ 700K /day (for prod. of 7,000bbls/day)

## Slide 4: Deposition mechanism
advection
diffusion

## Slide 5: Mathematical model
Precipitation &
Re-dissolution kinetics:
Dimensionless parameters:
Initial & boundary condition:
Kurup, A.S. et al., Energy & Fuels. 2011, 25, 4506–4516

## Slide 6: ADEPT simulator structure
Thermodynamic module
Deposition
module
Composition,
Liquid density,
Bubble point,
GOR, AOP, SARA
Asphaltene instability,
Ceq
Deposition
profile,
Thickness,
Pressure drop
Kinetic parameters
Operational conditions
Ceq
P-T profile in wellbore/pipeline
AOP--- Asphaltene onset pressure
Ceq --- Asphaltene equilibrium concentration

## Slide 7: Thermodynamic modeling
Appropriate Parameters
① Characterization / Recombination
②Tuning parameters to match Pb, liquid density, AOP
③Phase behavior prediction
④ Ceq calculation with P-T profile input
MW & mass percentages of all (Pseudo-) components
Asphaltene instability
Asphaltene equilibrium concentration, Ceq
Fluid composition, GOR, SARA
Deposition module

## Slide 8: Deposition modeling
The kinetic constant of deposition in capillary-scale
⑤ determine kp & kag using reaction model
⑥fitting kd(cap) to reproduce capillary deposition flux
⑦scaling up of kd(cap) to k*d
The kinetic constants of precipitation and aggregation
The kinetic constant of deposition in field-scale
Asphaltene deposition flux, thickness, pressure drop
The asphaltene precipitated amounts
Thermodynamic module
⑧input Ceq , kp , kag , k*d , operational conditions

## Slide 9
field case 1

## Slide 10: Deepwater Gulf of Mexico wellbore
  Wellbore pressure loss is approximately 10 psi per day in the first several weeks after wellbore wash;
  GOR decreases 60 ScF / STB over 4 months;
  GOR increases with gas injection;
  GOR sensitivity analysis is needed.

## Slide 11: Phase behavior prediction(wellbore)
Chart: T / F
| 100 | 120 | 140 | 160 | 184 | 200 | 220 | 240 | 260 | 280 | 300
onset P @GOR=669 | 8510 | 5810 | 4330 | 3760 | 3310 | 3030 | 2870 | 2800 | 2770
bubble P @GOR=669 | 2080 | 2150 | 2210 | 2270 | 2340 | 2380 | 2420 | 2460 | 2500 | 2520 | 2550
lower onset P @GOR=669 | 940 | 1180 | 1410 | 1630 | 1860 | 2000 | 2140 | 2260 | 2350 | 2410 | 2440
P-T trace | 8255 | 8015.32 | 7775.64 | 7535.96 | 7296.28 | 7056.6 | 6816.92 | 6577.24 | 6337.56 | 6097.88 | 5858.2 | 5618.52 | 5378.84 | 5139.16 | 4899.48 | 4659.8 | 4420.12 | 4180.44 | 3940.76 | 3701.08 | 3461.4 | 3221.72 | 2982.04 | 2742.36 | 2502.68 | 2263
onset P- exp. @GOR=669 | 4400
bubble P-exp. @GOR=669 | 2263
PC-SAFT EoS (VLXE / Multiflash / PVTsim)

## Slide 12: Phase behavior prediction(wellbore)
Chart: T / F
| 100 | 120 | 140 | 160 | 184 | 200 | 220 | 240 | 260 | 280 | 300
onset P @GOR=1000 | 10650 | 8830 | 7530 | 6750 | 6240 | 5910 | 5700
onset P @GOR=669 | 8510 | 5810 | 4330 | 3760 | 3310 | 3030 | 2870 | 2800 | 2770
onset P @GOR=549 | 7730 | 4660 | 3280 | 2390 | 2070 | 2100 | 2140 | 2170 | 2190 | 2210
bubble P @GOR=1000 | 2750 | 2820 | 2890 | 2960 | 3040 | 3080 | 3130 | 3170 | 3210 | 3240 | 3260
bubble P @GOR=669 | 2080 | 2150 | 2210 | 2270 | 2340 | 2380 | 2420 | 2460 | 2500 | 2520 | 2550
bubble P @GOR=549 | 1800 | 1860 | 1920 | 1970 | 2030 | 2070 | 2100 | 2140 | 2170 | 2190 | 2210
lower onset P @GOR=1000 | 820 | 1050 | 1260 | 1460 | 1690 | 1820 | 1960 | 2070 | 2160 | 2230 | 2270
lower onset P @GOR=669 | 940 | 1180 | 1410 | 1630 | 1860 | 2000 | 2140 | 2260 | 2350 | 2410 | 2440
lower onset P @GOR=549 | 940 | 1230 | 1480 | 1700 | 1940 | 2070 | 2100 | 2140 | 2170 | 2190 | 2210
P-T trace | 8255 | 8015.32 | 7775.64 | 7535.96 | 7296.28 | 7056.6 | 6816.92 | 6577.24 | 6337.56 | 6097.88 | 5858.2 | 5618.52 | 5378.84 | 5139.16 | 4899.48 | 4659.8 | 4420.12 | 4180.44 | 3940.76 | 3701.08 | 3461.4 | 3221.72 | 2982.04 | 2742.36 | 2502.68 | 2263
onset P- exp. @GOR=669 | 4400
bubble P-exp. @GOR=669 | 2263
GOR
GOR
Notes: .

## Slide 13: Extract kp & kag
Aging Time (hour) | Precipitate amount (g)
0.166667 | 0.0132
0.333333 | 0.0165
0.5 | 0.0169
2 | 0.0167
4 | 0.0172
7.5 | 0.0187
12 | 0.0182
24 | 0.02
kp / s-1 | 2.5×10-2
kag / s-1 | 1.7×10-3
Batch experimental results from NMT
Chart: Time, hr
| 0.16666666666666666 | 0.33333333333333331 | 0.5 | 1 | 2 | 4 | 7.5 | 12 | 24
measured | 0.42557 | 0.53196 | 0.54486 | 0.59966 | 0.53841 | 0.55453 | 0.60289 | 0.58677 | 0.6448

## Slide 14: Capillary deposition test
Wang, J. X., et al., Dispersion Sci. Technol. 2004, 25, 287–298.

## Slide 15: Fitting kd(cap)
kd(cap) = 2.11×10-3 s-1
Fitting kd (cap) to make the peak of deposition flux curve predicted match the experimental observation.
Chart: tubing lenth / inch
Simulation with fitted kd (cap)
Expt

## Slide 16: Scale up kd(cap) to k*d
kd (cap)
k*d(mom) = 4.31×10-6 s-1
Kurup, A.S. et al., Energy & Fuels. 2012, 26 (9), pp 5702–5710

## Slide 17: Deposition flux prediction (wellbore)
Chart: Distance ( ft )
Chart: Deposition flux (g/cm2/s)
I
II
III
Precipitated particles
Flow out
Aggregation
Deposition
Flow in
CF-CEQ = 0
Re-dissolution starts

## Slide 18: Deposit thickness prediction (wellbore)
Chart: Distance / ft
14 days

## Slide 19: Frictional pressure drop (wellbore)
GOR SCF/STB | Frictional pressure drop Psi /day
549 | 9.45
669 | 10.10
1000 | 10.89
≈ 10 Psi / day (Based on 14 days) | 

## Slide 20
field case 2

## Slide 21: Field information (pipeline)
Asphaltene problem is reported.
The total pressure drop in the first 28 days is about 648 psi.
The asphaltene deposition situation must be estimated.
Pipeline | Gulf of Mexico
Pressure | 5,284 psi
Temperature | 177 ⁰F
Flow rate | 13482 bbl/day
Diameter | 5.137 inch 4.881 inch
length | 52389 ft

## Slide 22: Phase behavior prediction (pipeline)

## Slide 23: Kinetic parameters
Simulation with fitted kd (cap)
Expt
kp / s-1 | 1.32×10-3
kag / s-1 | 7.29×10-5
kd(cap) = 1.43×10-3 s-1
k*d(mom) | 3.25×10-6 s-1
k*d(lar) | 1.73×10-6 s-1
k*d(mt) | 4.50×10-7 s-1

## Slide 24: Simulation results
Chart: Distance (ft)
Boundary layer | Frictional ∆P (Psi)
Momentum | 700
Laminar | 605
Mass transfer | 519
Field data= 648 Psi (28days) | 

## Slide 25: Summary
    ADEPT simulator can successfully predict the asphaltene deposition in wellbore/pipeline.
    Onset pressure and bubble pressure increases significantly with GOR increases, but the effects on lower onset pressure can be neglected;
    Deposit location changes with GOR.

## Slide 26: Acknowledgments
Jeff Creek
Jianxin Wang
Andrew Yen
Sai Panuganti
Jill Buckley
Vargas Francisco