## Slide 1
Effects of Hardness and Cosurfactant on Phase Behavior of Alcohol-Free Alkyl Propoxylated Sulfate Systems
Maura C. Puerto, Clarence A. Miller and George J. Hirasaki
Rice University
Carmen Reznik, Sheila Dubey, Julian R. Barnes and Sjoerd vanKuijk Shell Global Solutions
Presented at Annual Meeting of Rice University Consortium
on Processes in Porous Media, April 21, 2014
Based on SPE 169096-MS presented at SPE Symposium on IOR
Tulsa, OK, April 14-16, 2014

## Slide 2
TOPICS 1 of 2
Slide 2
SPE 169096 – MS • Maura C Puerto
SO3-Na SO3-Na
R-CH2-CH2- CH –CH -CH2-CH2-R’ + R-CH2 – CH-CH= CH-CH2-R’
OH
Hydroxyalkane Sulfonates + Alkene Sulfonates
APS
AES
IOS
            Behavior of Surfactant Blends
            WOR ~1 with n-octane and its Aqueous Solutions
Alcohol Propoxy Sulfates
Alcohol Ethoxy Sulfates
Internal Olefin Sulfonate

## Slide 3
TOPICS 2 of 2
      Phase Behavior
    Optimal Blends with n-octane, a crude oil
    Injection Composition without oil
    Salinity Maps for variable salinity processes
Slide 3
SPE 169096 – MS • Maura C Puerto

## Slide 4
Slide 4
SPE 169096 – MS • Maura C Puerto
OBJECTIVE
Slide 4
SPE 169096 – MS • Maura C Puerto
Without adding alcohol, determine effect of hardness on equilibrium phase behavior for three blend types.
Challenge: Low-tension Oil-Water-Surfactant systems are suitable for injection when made as microemulsions but seldom suitable when made as aqueous solutions, which are often cloudy or form precipitates.
Blend | Research Focused on
APS/IOS15-18 | Finding aqueous single-phase solutions capable of generating low-tension in hard brines such as seawater
APS/APS | 
APS/AES | 

## Slide 5
Slide 5
SPE 169096 – MS • Maura C Puerto
Experimental Highlights
Wt% Salt | SW | 
NaCl | 2.9 | 4.0
CaCl2 | 0.13 | 
MgCl2 6H2O | 1.12 | 
TDS (g/L) | 35.5 | 40.0
Ionic strength mol/L | 0.70 | 0.68
Typical brine composition Oil Test Temperature
n-octane ambient to <60°C
a crude oil
0 1 2 3 4 5 6 7 8 9 10
SW 9/1 8/2 7/3 6/4 5/5 6/4 7/3 8/2 9/1 15%NaCl
~9weeks of equilibration
Salinity Scan: SW/15%NaCl mixtures, WOR~1
2%total b-C677P/IOS_1/1 by wt, n-C8, ~25°C

## Slide 6
Slide 6
SPE 169096 – MS • Maura C Puerto
Surfactants Used in Blend Scans
Hydrophobe | Propoxy Groups |  |  |  | Ethoxy Groups | Named
Sulfates |  |  |  |  |  | 
Branched C16-17 |  | 7 |  | 0 |  | b-C67 7P
Lower branched C12-13 |  | 7 |  | 0 |  | b-C23 7P
Higher branched C12-13 |  | 7 |  | 0 |  | B-C23 7P
Lower branched C12-13 |  | 0 |  | 7 |  | b-C23 7E
Higher branched C12-13 |  | 0 |  | 7 |  | B-C23 7E
Sulfonate |  |  |  |  |  | 
Internal Olefin Sulfonate 15-18 |  |  |  |  |  | IOS
Bø = Optimal Blend
Blend Scan
b-C67 7P/IOS
2wt% total
2*SW, 25°C,
WOR~1, n-C8

## Slide 7
=
Hard and Soft brines of Equal Ionic Strength
=
Optimal Blend Ratios : APS/IOS
High oil & brine solubilization parameters near optimal conditions so, highly promising for EOR processes
2*, 3*SW reveal tolerance to both salinity & hardness
Unclear Aqueous Solutions 2*, 3*SW or 8 ,12% NaCl

## Slide 8
Slide 8
SPE 169096 – MS • Maura C Puerto
Optimal Blend Ratios : APS/IOS
50°C | b-C67 7P : IOS | Bø | Not done | 45:55 | 45:55 | 25:75 | 35:65
 |  | V/Vs |  | 16 | 15 | 11 | 10
 | b-C23 7P : IOS | Bø | Not done | 80:20 | 75:25 | 45:55 | 45:55
 |  | V/Vs |  | 1ø | 22 | 11 | 11
 | B-C23 7P : IOS | Bø | Not done | 65:35 | 65:35 | 35:65 | 35:65
 |  | V/Vs |  | 17 | 17 | 18 | 18
=
=

## Slide 9
Slide 9
SPE 169096 – MS • Maura C Puerto
Aqueous Solubility Map for SW: APS/IOS at 25ºC
Generally difficult to find clear aqueous solution at optimal
Precipitation of IOS above ~30% is limitation here
Chart: 
| APS | 9/1 | 8/2 | 7/3 | 6/4 | 5/5 | 4/5 | 3/7 | 2/8 | 1/9 | IOS
Clear | 1 | 1 | 1
Clear | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Clear | 2.5 | 2.5 | 2.5 | 2.5 | 2.5
Cloudy | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5
Clear | 4.5 | 4.5 | 4.5 | 4.5
Cloudy | 4.5 | 4.5 | 4.5 | 4.5 | 4.5 | 4.5 | 4.5

## Slide 10
Chart: Formation Brine = 3*SW
| 75.0 | 50.0 | 25.0

 | 15 | 35 | 45


WINSOR TYPE I
WINSOR TYPE II
Dilution path
Possible Aqueous Injection blend range:
65/35 - 85/15
of b-C67 7P/IOS
Too much IOS , too high IFT
Too much APS, transition to Winsor Type II :
surfactant will be lost by partitioning into oil, making heavy emulsion, etc.
Salinity Map for Variable Salinity: APS/IOS at 25°C
Slide 10
SPE 169096 – MS • Maura C Puerto

## Slide 11
Slide 11
SPE 169096 – MS • Maura C Puerto
Blends of APS/APS and APS/AES at 250C
Example : b-C23 7E and b-C67 7P
2% Surfactant
WOR ~ 1
SeaWater
n-Octane
1% Surfactant
in SW, Aqueous
Solutions
Cloudy
Clear

## Slide 12
Slide 12
SPE 169096 – MS • Maura C Puerto
Model Oil n-octane and Crude oil at ~50ºC
Optimal AES/APS ratio as a function of Oil Molar Volume
Phase Behavior b-C237P/B-C137E:
90 88 86 84 82 80
The small difference indicates that n-octane is a good choice of model oil to be used for initial screening purposes in this system.
Chart: OMV, cm3/g-mole ~ 50°C
| 168.7
 | 13
 | 87 | 83

## Slide 13
Slide 13
SPE 169096 – MS • Maura C Puerto
Aqueous Solubility Map for SW: 1%APS/APS 25ºC
Ethoxy or Propoxy groups on both surfactants provide tolerance to salinity and hardness, that is greater than when one surfactant is IOS
Chart: 
| 10/0 | 9/1 | 8/2 | 7/3 | 6/4 | 5/5 | 4/6 | 3/7 | 2/8 | 1/9 | 0/10
 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 1
 | 1
 | 2
 | 4
 | 3
ø

## Slide 14
Slide 14
SPE 169096 – MS • Maura C Puerto
APS/AES blend produced Low IFT against crude oil,
as expected from its phase behavior with n-octane
Phases selected for IFT measurements from phase behavior salinity scan with crude oil:
1% b-C23 7P and B-C237E
SW at ~50°C.
Shows Winsor III behavior.
IFT measured between excess oil and brine phases = ~10-2 mN/m.
Based on discussion by Sottmann and Strey (1997), IFT values of microemulsion/oil and microemulsion/brine interfaces < 10-2 mN/m
Substantial residual oil should be displaced for these conditions.

## Slide 15
Slide 15
SPE 169096 – MS • Maura C Puerto
Conclusions 1of 3
Blends of branched APSs with IOS15-18
Form alcohol-free microemulsions with n-octane having high oil solubilization at optimal conditions up to 3*SW and 50ºC.
Have similar optimal blend ratios for same ionic strength of 2*SW, 3*SW and NaCl solutions at 25ºC, 50ºC.
  oil-free aqueous solutions unsuitable for injection (cloudy and/or precipitate) for same conditions.
In SW aqueous solutions unsuitable for injection beyond ~30% IOS at 25ºC.

## Slide 16
Slide 16
SPE 169096 – MS • Maura C Puerto
Conclusions 2 of 3
Blends of branched APSs with other APSs or AESs
Appear more favorable than APS/IOS for having aqueous solutions suitable for injection over a range of optimal blend ratios, at least at low temperatures in SW.
2. Formed alcohol-free microemulsions promising for EOR with a crude oil in SW at ~50ºC with two APS/AES blends
3. Had cloudy aqueous solutions at opt. blend ratios with crude oil at 50C but clear at slightly different ratios exhibiting lower phase microemulsions.

## Slide 17
Slide 17
SPE 169096 – MS • Maura C Puerto
Conclusions 3 of 3
    Salinity maps as shown here for n-octane but not shown for crude oil should prove useful in designing IOR processes where compositions of injection and formation brines differ.

## Slide 18
Grateful to Shell Global Solutions for funding this research
Slide 18
Thank You
Questions?

## Slide 19
Slide 19
SPE 169096 – MS • Maura C Puerto
Salinity Map for a Crude oil: AES/APS at ~50°C
SeaWater and
NaCl-only brine
of same Ionic Strength

## Slide 20
Slide 20
SPE 169096 – MS • Maura C Puerto
Salinity Map for SW and Crude oil: 1% b-C237P/ b-C677P
all Clear at 25ºC
~50ºC
Chart: 
| b-C23 7E | 9/1 | 8/2 | 7/3 | 6/4 | 5/5 | 4/6 | 3/7 | 2/8 | 1/9 | b-C67 7P
Clear | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Clear | 2 | 2 | 2 | 2 | 2 | 2 | 2
Clear | 3 | 3 | 3 | 3 | 3
Cloudy | 1 | 1 | 1
Cloudy | 3 | 3 | 3 | 3 | 3 | 3
Cloudy | 2 | 2 | 2 | 2
Bø