## Slide 1: Effect of Gas Type and Composition on Foam Rheology in Porous Media for EOR
Yongchao Zeng
Ali Akbar Eftekhari┴, Aarthi Muthuswamy†, Sebastien Vincent-Bonnieu‡,
Rouhi Farajzadeh‡┴*, Sibani L. Biswal†*, and George J. Hirasaki†*
†Rice University, 6100 Main St., MS-362, Department of Chemical and Biomolecular Engineering, Houston, TX, 77005 USA.
‡Shell Global Solutions International, 2288GS Rijswijk, the Netherlands
┴Delft University of Technology, Delft, 2628CN, the Netherlands.
19th Consortium

## Slide 2: Gas Supply for Foam EOR
CO2
N2
CH4/CO2
Flue Gas
CH4
Bentheimer Sandstone | Parameters
Diameter | 3.8 cm
Length | 17.0 cm
Porosity | 21.0 %
Pore Volume | 40.5 cm3
Permeability (DI water) | 2.3 Darcy
Gas Possibilities for Foam EOR
Core Sample

## Slide 3: Experiment Setup Scheme

## Slide 4: Materials and Conditions
Chart: Brine Composition
| Na | Mg | Ca | K | Cl | SO4
Baronia Field | 10700 | 1214 | 395.1 | 353.2 | 19907.3 | 2600
World's Average | 10736.08 | 1302 | 420 | 311.5 | 19272.32 | 2705.5
Experiment Conditions | 
Total Interstitial Velocity | 20 ft/day
Temperature | ~20 oC
Back Pressure | 21 bar
Surfactant AOS C14-16: 1 wt%
  Successfully applied to pilot test in Snorre field in North Sea
Brine Composition:
  Baronia field sea water Salinity

## Slide 5: Foam Strength Comparison
Steady State Foam Strength for Pure Gases
N2 > CH4 > CO2

## Slide 6: Three Hypotheses
Hypothesis I (Stability of Lamella)
Different types of gas will affect the stability of lamella by changing the disjoining pressure.
Hypothesis II (Gas Solubility)
Different types of gas have varied solubility in aqueous phase. For gas with high solubility, the actual foam quality is lower than the injected quality. Thus the foam apparent viscosity is different.
Hypothesis III (Diffusion Coarsening)
Different types of gas have varied permeability through the lamella thus changing the rate of mass transfer between small and large bubbles.

## Slide 7: Hypothesis I
Hypothesis I: Stability of Lamella
Disjoining Pressure
  the change in surface energy per unit area with change in distance of the pair of interfaces
DLVO Theory
Israelachvili, Jacob 1991 Intermolecular and Surface Forces. Second Edition. Academic Press.

## Slide 8: Hypothesis I
Electrostatic Repulsion Component
Physical Model: Two planar surfaces
There is no direct evidence or convincing argument indicating that gas type can affect the electrostatic repulsion part
Israelachvili, Jacob 1991 Intermolecular and Surface Forces. Second Edition. Academic Press.

## Slide 9: Hypothesis I
Physical Model: Two planar surfaces
Electrostatic Repulsion Component
Exerowa, D., T. Kolarov, and Khr. Khristov 1987 Direct Measurement of Disjoining Pressure in Black Foam Films. I. Films from an Ionic Surfactant. Colloids and Surfaces 22(2): 161–169.

## Slide 10: Hypothesis I
Van de Waals Component
Gas Type | a /Pa.m6.mol-2 | b / m3/mol | σvw / Å
N2 | 0.141 | 3.91E-5 | 4.99
CH4 | 0.228 | 4.28E-5 | 5.14
CO2 | 0.364 | 4.27E-5 | 5.14
Gas Type | c / J.m6
N2 | 2.3E-77
CH4 | 4.1E-77
CO2 | 6.5E-77
Van der Waals Parameters
Van der Waals Pair Potential Coefficient
Assumption: Van der Waals EOS applies to all types of gases
Israelachvili, Jacob 1991 Intermolecular and Surface Forces. Second Edition. Academic Press.
Zhu, Wentao 2008 Physical Chemistry. Tsinghua University Press

## Slide 11: Hypothesis I
Van de Waals Interaction across Vacuum
Gas Type | A11 ( J) 21 bar 20 ℃
N2 | 3.8E-22
CH4 | 7.9E-22
CO2 | 20.3E-22
Conventional Hamaker Constant
Israelachvili, Jacob 1991 Intermolecular and Surface Forces. Second Edition. Academic Press.

## Slide 12: Hypothesis I
Van de Waals Interaction across Water Film
Material | A131 ( J ) 21 bar 20 ℃
N2¦Water¦N2 | 3.40E-20
CH4¦Water¦CH4 | 3.29E-20
CO2¦Water¦CO2 | 3.15E-20
Assumption: Combining relation applies
Israelachvili, Jacob 1991 Intermolecular and Surface Forces. Second Edition. Academic Press.

## Slide 13: Hypothesis I
Van de Waals Component
Van der Waals Component
CO2 > CH4 > N2

## Slide 14: Hypothesis I
Disjoining Pressure Based on DLVO Theory
Disjoining pressure calculated from different Hamaker constants shows that CO2 has the most stable foam whereas N2 has the least stable foam, which is contrary to our experimental observation.
The van der Waals property of gas does not explain the different foam strength with respect to different gas type.

## Slide 15: Hypothesis II
Hypothesis II: Gas Solubility
Gas Type | Mole Fraction Solubility X1 (20 ℃, 1 bar)
N2 | 1.2E-5
CH4 | 2.6E-5
CO2 | 61.5E-5
CO2 foam
CO2 foam with surfactant solution saturated with CO2 at 21 bar (13.24 bar CO2 was dissolved in 2L surfactant solution at 21 bar)
CO2 foam with increased gas flow rate to compensate the dissolved CO2 in surfactant solution (assuming local equilibrium; CO2 solubility model provided by Zhenhao Duan)
What if we compensate the dissolved gas in aqueous phase?

## Slide 16: Hypothesis II
More gas is required to foam as the gas solubility in the aqueous solution is high. Because the surfactant solutions were not saturated, the gas dissolves in the solution, which will make the actual quality lower than the injected quality.
Gas solubility has a significant effect on foam strength in low quality region whereas the effect in high quality region is negligible.

## Slide 17: Hypothesis III
Hypothesis III: Diffusion Coarsening
Gas Type | kfilm* (m/s)
N2 | 0.13
Flue Gas | 0.16
CH4 | 0.30
(50% CH4 & 50% CO2) | 0.58
CO2 | 7.85
Gas Diffusion across Thin Film
Princen, H.M., and S.G. Mason 1965 The Permeability of Soap Films to Gases. Journal of Colloid Science 20(4): 353–375.
Farajzadeh, Rouhi 2014 Effect of Gas Type and Composition on Macroscopic Properties of Foam.

## Slide 18: Hypothesis III
Effect of Gas Composition
The mixture of gases usually have approximately the same foam strength as the less soluble gas.
When adding a second component into the gas, the system increases one degree of freedom which will allow bubbles to coexist at different pressures. This is the reason for adding non-condensable gas in steam foams.

## Slide 19: Hypothesis III
Experimentally relative foam strength shows a significant dependence on permeability of the film. Foam strength decays with the increase in film permeability.
Different types of gas have varied film permeability. The difference in film permeability changes the rate of gas diffusion. Thus bubbles coarsen at different rate.

## Slide 20: Hypothesis III
Controversial Gas Diffusion for Porous Media Foam
Time 1
Time 2
Time 3
Time 4
Direct Evidence: Foam Flow in Micro-model (By Charles Conn)
Diffusion-driven coarsening was observed to be the dominant foam destruction mechanism.

## Slide 21: Conclusion
Under our experiment condition, the van der Waals property of different gases in the disjoining pressure does not account for the different foam strength in porous media.
Compensating dissolved CO2 in aqueous phase will increase foam strength in low quality regime however having negligible effect in high quality regime.
The mixture of gases usually has approximately the same foam strength as the less soluble gas.
Different types of gas have varied permeability through lamella. Gas diffuses at different rate. Consequently the rate of foam coarsening is different. Thus different gas has different foam strength.

## Slide 22: Acknowledgement
We acknowledge financial support from
Petroliam Nasional Berhad
(PETRONAS, Kuala Lumpur, Malaysia)
Shell Global Solutions International
(Rijswijk, the Netherlands).
Rice University Consortium for Processes in Porous Media (Houston, TX, USA)

## Slide 23: Thank you